## Slide 1
CompTIA A+
CORE 1 · CORE 2
220-1101 · 220-1102
COURSE SLIDES · WSQ
CompTIA Certified A+ Training (Core 1 and Core 2)
WSQ Course Code: TGS-2024048317
Conducted by Tertiary Infotech Academy Pte Ltd · UEN 201200696W
Version v7.1 · 19 August 2026
© 2026 Tertiary Infotech Academy Pte Ltd. All rights reserved. · www.tertiarycourses.com.sg

## Slide 2
COURSE ADMINISTRATION
Welcome & Housekeeping
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
2

## Slide 3
TRAQOM · SSG DIGITAL ATTENDANCE
Digital Attendance (Mandatory)
1
Three times a day
Take the AM, PM and Assessment digital attendance — mandatory for every WSQ-funded course.
2
Trainer shows the QR
The trainer or administrator displays the digital attendance QR code from the SSG portal.
3
Scan and submit
Scan the QR code with your mobile phone camera and submit your attendance.
4
75% minimum
A minimum of 75% attendance is required to be eligible for assessment and funding.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
3

## Slide 4
YOUR TRAINER · GENERAL
About the Trainer
?
Your Trainer
General Trainer template — to be completed by the trainer
NAME
____________________________________________
TITLE / DESIGNATION
____________________________________________
QUALIFICATIONS
____________________________________________
AREAS OF EXPERTISE
____________________________________________
TRAINING & INDUSTRY EXPERIENCE
____________________________________________
CONTACT
____________________________________________
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
4

## Slide 5
YOUR TRAINER
About the Trainer
AA
Dr Alfred Ang
Principal Trainer Tertiary Infotech Academy Pte Ltd
ROLE
Principal Trainer, Tertiary Infotech Academy Pte Ltd
EXPERTISE
IT infrastructure support, networking, systems administration and cybersecurity.
DELIVERS
WSQ CompTIA courses including A+, Network+, Security+, Linux+ and Cloud+.
FOUNDER
Founder and lead instructor at Tertiary Infotech / Tertiary Courses.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
5

## Slide 6
ICE-BREAKER
Let's Know Each Other
• Your name, organisation and role.
• Your current experience supporting PCs, laptops, mobile devices or networks.
• Whether you are working towards the CompTIA A+ certification exams.
• What you most want to be able to do confidently by the end of this course.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
6

## Slide 7
HOUSEKEEPING
Ground Rules
1
Set your mobile phone to silent mode.
2
Participate actively — no question is too small.
3
Mutual respect: agree to disagree.
4
One conversation at a time.
5
Be punctual; return from breaks on time.
6
75% attendance is required for funding.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
7

## Slide 8
LMS / TMS · lms-tms.tertiaryinfotech.com
Download Your Course Material
1
1 · Go to the LMS portal
Open https://lms-tms.tertiaryinfotech.com in your browser.
2
2 · Log in
Sign in with the account e-mail you used to register for this course.
3
3 · Open this course
Select 'CompTIA Certified A+ Training (Core 1 and Core 2)'.
4
4 · Download
Download the Trainer Slides, Learner Guide and Lesson Plan (PDF).
5
5 · Get the labs
Open the lab repository on GitHub — the link is on your course page.
6
6 · Keep them open
You may use these materials during the open-book assessment.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
8

## Slide 9
SKILLS FRAMEWORK · KNOWLEDGE (ASSESSED BY THE WA)
Skills Framework Alignment
1
TSC Title
Infrastructure Support
2
TSC Code
ICT-OUS-3007-1.1
3
K1
Diagnostic tools and processes to identify technical issues or disruptions in network infrastructure
4
K2
Infrastructure and network configuration techniques
5
K3
Troubleshooting techniques for infrastructure technical issues and problems
6
K4
Potential benefits and impact of infrastructure upgrades and improvements
7
K5
Sources of information for the development of infrastructure user guides and documentation
8
K6
Types and purposes of system tests for infrastructure operating requirements
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
9

## Slide 10
SKILLS FRAMEWORK · ABILITIES (ASSESSED BY THE PP)
Skills Framework Alignment — Abilities
1
A1
Diagnose technical issues in network operations
2
A2
Implement procedures to resolve root causes of technical issues
3
A3
Troubleshoot technical issues in infrastructure systems
4
A4
Perform advanced infrastructure configurations
5
A5
Develop action plans for infrastructure upgrades
6
A6
Propose infrastructure improvement ideas based on user needs
7
A7
Test infrastructure systems against operating requirements
8
A8
Organise information for the development of user guides
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
10

## Slide 11
WHAT YOU'LL ACHIEVE
Learning Outcomes
1
LO1 · Diagnose and resolve
Diagnose technical issues in network operations and implement procedures to resolve root causes.
2
LO2 · Troubleshoot and configure
Troubleshoot technical issues and perform advanced infrastructure configurations.
3
LO3 · Plan upgrades
Develop action plans for upgrades and propose improvement ideas based on user needs.
4
LO4 · Test and document
Test infrastructure systems and organise information for developing user guides.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
11

## Slide 12
CORE 1 + CORE 2 · 54 HANDS-ON LABS
Course Outline — Nine Domains Across Five Days
1
Topic 01 — Mobile Devices (Core 1)
Laptop hardware · display components · accessories and ports · cellular and wireless · MDM and synchronisation
2
Topic 02 — Networking (Core 1)
Protocols and ports · network devices · wireless standards · SOHO networks · IP addressing · networking tools
3
Topic 03 — Hardware (Core 1)
Cables and connectors · RAM · storage and RAID · motherboards · CPUs and cooling · power supplies · printers
4
Topic 04 — Virtualization and Cloud Computing (Core 1)
Hypervisors · virtual machines · resource requirements · cloud models · shared resources and metered use
5
Topic 05 — Hardware and Network Troubleshooting (Core 1)
The CompTIA troubleshooting methodology · POST and boot faults · storage and RAID · display faults · printer and network symptoms
6
Topic 06 — Operating Systems (Core 2)
Windows editions and installation · command line · Windows tools and MMC · file systems · macOS and Linux
7
Topic 07 — Security (Core 2)
Physical and logical security · authentication and MFA · wireless security · malware · social engineering · workstation and mobile hardening
8
Topic 08 — Software Troubleshooting (Core 2)
Windows OS symptoms · recovery tools · malware removal · browser problems · mobile OS and application faults
9
Topic 09 — Operational Procedures (Core 2)
Documentation and ticketing · asset management · change management · backup and recovery · safety and environment · professionalism · scripting and remote access
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
12

## Slide 13
EXAM DOMAIN WEIGHTING
CompTIA A+ Core 1 (220-1101) Exam Weighting
Chart: 
| Mobile Devices | Networking | Hardware | Virtualization & Cloud | HW/Network Troubleshooting
Share of Core 1 exam (%) | 13 | 23 | 25 | 11 | 28
WHAT THE DATA SHOWS
Hardware and Network Troubleshooting is the largest Core 1 domain at 28%, and Hardware follows at 25% — more than half the Core 1 exam sits in these two domains, so that is where your revision time should go.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
13

## Slide 14
EXAM DOMAIN WEIGHTING
CompTIA A+ Core 2 (220-1102) Exam Weighting
Chart: 
| Operating Systems | Security | Software Troubleshooting | Operational Procedures
Share of Core 2 exam (%) | 28 | 28 | 23 | 21
WHAT THE DATA SHOWS
Core 2 is the most evenly weighted of the two exams — Operating Systems and Security tie at 28% each, and no domain falls below 21%, so none can safely be skipped.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
14

## Slide 15
SCHEDULE
Lesson Plan — 5 Days, 8 hours/day
Days 1–3 · Core 1
Days 4–5 · Core 2
• Day 1 — Mobile Devices and Networking
– Digital Attendance (AM) · Introductions · Learning Outcomes
– Topic 1: Mobile Devices (Labs 1–4)
– Topic 2: Networking (Labs 5–11)
• Day 2 — Hardware, Virtualization and Cloud
– Topic 3: Hardware (Labs 12–18)
– Topic 4: Virtualization and Cloud (Labs 19–21)
• Day 3 — Hardware and Network Troubleshooting
– Topic 5: Hardware and Network Troubleshooting (Labs 22–28)
• Day 4 — Operating Systems and Security
– Topic 6: Operating Systems (Labs 29–36)
– Topic 7: Security begins (Labs 37–40)
• Day 5 — Software Troubleshooting, Operational Procedures and Assessment
– Topic 7: Security concludes (Labs 41–44)
– Topic 8: Software Troubleshooting (Labs 45–49)
– Topic 9: Operational Procedures (Labs 50–54)
– TRAQOM Survey · Digital Attendance (Assessment)
– Final Assessment (WA + PP)
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
15

## Slide 16
NO INSTALL REQUIRED
Your Lab Toolkit — Everything Runs in the Browser
1
IP Calculator
Browser subnet calculator for IPv4 and IPv6 — CIDR, netmask, network and broadcast addresses, usable host ranges and batch processing with CSV export.
2
PCAP Analyzer
Browser packet-capture analyser — protocol distribution, top talkers, top conversations and a packet table with per-packet detail. Files are parsed locally and never uploaded.
3
Cybersecurity Simulator
Safe threat-simulation lab covering phishing, XSS, SQL injection, password strength, malware, ransomware, social engineering and data leakage.
4
RegexLab
Live regular-expression tester with flags, match explanation and substitution — used to filter and parse support logs.
5
Killercoda Ubuntu Playground
Free browser-based Ubuntu terminal with root access — no install required. Used for every Linux command-line lab in this course.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
16

## Slide 17
BOOKMARK THESE NOW
Lab Tool Links
1
IP Calculator
https://alfredang.github.io/ipcalculator/
2
PCAP Analyzer
https://alfredang.github.io/pcapanalyzer/
3
Cybersecurity Simulator
https://alfredang.github.io/cybersecuritysimulator/
4
RegexLab
https://alfredang.github.io/regexgenerator/
5
Killercoda Ubuntu Playground
https://killercoda.com/playgrounds/scenario/ubuntu
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
17

## Slide 18
BEFORE YOU START
Briefing for Assessment
1
Do · Clear your desk
Place phones and other materials under the table or on the floor.
2
Don't · No recording
No photos or recording of assessment scripts.
3
Don't · No discussion
Work individually — no discussion during the assessment.
4
Do · Black or blue pen
Use a black or blue pen for hard-copy assessments.
5
Don't · No correction fluid
No liquid paper or correction tape may be used.
6
Do · Stop on time
Scripts are collected when time is up.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
18

## Slide 19
FINAL ASSESSMENT
Assessment
1
Written Assessment (WA)
Short-Answer Questions (SAQ) · 1 hour · open book. Tests the underpinning knowledge taught across the nine domains.
2
Practical Performance (PP)
Hands-on support, configuration and troubleshooting tasks · 1 hour · open book. Tests the ability you built in the labs.
3
Open book
You may use the course slides, the Learner Guide and approved materials only.
4
Eligibility
A minimum of 75% attendance is required to be eligible for assessment and funding.
5
Result
You are assessed as Competent (C) or Not Yet Competent (NYC) on each instrument.
6
Appeals
An appeal process is available if you wish to contest an assessment outcome.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
19

## Slide 20
ON ASSESSMENT DAY
Assessment Flow
1
TRAQOM survey
Scan the QR code on the LMS
2
Digital attendance
Scan the SSG assessment QR
3
Sit WA then PP
Open book · 1 hour each
4
Submit on the LMS
Upload your completed answers
5
Sign the record
Sign the Assessment Summary Record
REMEMBER
All five steps are mandatory for WSQ funding — missing the digital attendance or the TRAQOM survey can invalidate your claim.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
20

## Slide 21
WSQ FUNDING
Criteria for Funding
1
Attendance
A minimum attendance rate of 75%, based on the SSG Digital Attendance record.
2
Assessment
Complete both assessment components and be assessed as 'Competent'.
3
Digital attendance
Scan the SSG QR code for AM, PM and Assessment on every training day.
4
TRAQOM survey
Complete the mandatory TRAQOM course feedback survey on the LMS.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
21

## Slide 22
EXAM PREPARATION · exams.tertiaryinfotech.com
Practice Exam — Before You Sit the Real Thing
1
Where
https://exams.tertiaryinfotech.com
2
Which exam
CompTIA A+ Core 1 and Core 2 Practice Exam
3
Why it helps
Sit the practice exam before your certification attempt. It mirrors the Core 1 and Core 2 domain weightings so your score by domain shows exactly where to revise.
4
How to use it
Sit it once cold to find your weak domains, revise those, then sit it again to confirm the gap has closed.
5
Core 1 target
Aim for a consistent pass across all five Core 1 domains before booking 220-1101.
6
Core 2 target
Aim for a consistent pass across all four Core 2 domains before booking 220-1102.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
22

## Slide 23
CORE CONCEPTS
The Foundations Behind Every Domain
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
23

## Slide 24
WHY THIS COURSE
A+ is a troubleshooting certification.
Every domain in both exams ultimately asks the same question: given these symptoms, what has actually failed, and what do you do about it?
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
24

## Slide 25
THE FRAMEWORK BEHIND EVERY TROUBLESHOOTING LAB
The CompTIA Six-Step Troubleshooting Methodology
1
Identify the problem
Question the user · what changed · back up first
2
Establish a theory
Question the obvious · rank by likelihood
3
Test the theory
Confirm or reject · escalate if needed
4
Plan and implement
Vendor guidance · state the rollback
5
Verify and prevent
Full functionality · preventive measures
6
Document
Findings · actions · outcomes
EXAMINABLE IN ORDER
The steps are tested in sequence. Documenting is step six and is not optional — an undocumented fix teaches the organisation nothing and is invisible at audit.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
25

## Slide 26
TWO EXAMS, ONE CERTIFICATION
Core 1 vs Core 2 — What Each Exam Tests
Dimension
Core 1 (220-1101)
Core 2 (220-1102)
Focus
Physical infrastructure and connectivity
Software, security and process
Largest domain
Hardware & Network Troubleshooting (28%)
Operating Systems and Security (28% each)
Typical task
Diagnose a machine that will not POST
Remove malware and harden the workstation
Tools
Multimeter, cable tester, toner probe
Task Manager, MMC, command line
Mindset
What component failed?
What changed, and is it safe?
WHEN IT MATTERS You must pass BOTH exams to earn the A+ certification. They are sat separately and can be taken in either order, though Core 1 first is the conventional path.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
26

## Slide 27
THE FIRST FORK IN EVERY DIAGNOSIS
Is This a Hardware or a Software Problem?
Does the fault survive a clean boot from other media?
YES — suspect hardware
The fault follows the machine rather than the installed system. Move to component isolation: reseat, substitute a known-good part, and test the minimum configuration.
NO — suspect software
The hardware is capable, so the installed OS, a driver, an update or malware is responsible. Move to the recovery ladder starting at the least destructive rung.
This single question saves more time than any other in support work — it halves the search space before you touch a screwdriver or a recovery tool.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
27

## Slide 28
ALWAYS WORK BOTTOM-UP
The Layers You Diagnose Through
1
Physical
Is it powered, plugged in, and does the link light show carrier? Nothing above this layer works until this one does.
2
Addressing
Does the host have a valid IP, mask and gateway — or an APIPA address meaning DHCP never answered?
3
Routing
Is there a default route, and does the gateway respond? This separates a local fault from an internet fault.
4
Name resolution
Does DNS resolve? A host that pings an IP but not a name has a DNS fault and nothing else.
5
Application
Is the service listening, is the port reachable, and is the firewall permitting it?
6
The user
What did they actually do, and what changed? Most faults are a recent change rather than a spontaneous failure.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
28

## Slide 29
EXAMINABLE PORT PAIRS
Secure and Insecure Protocol Pairs — Know These On Sight
Insecure
Port
Secure replacement
Port
Why it matters
Telnet
23
SSH
22
Telnet sends credentials in clear text
FTP
20/21
SFTP
22
FTP sends credentials and data in clear text
HTTP
80
HTTPS
443
HTTP has no encryption or server authentication
SNMPv1/v2
161/162
SNMPv3
161/162
Only v3 encrypts and authenticates
POP3
110
POP3S
995
Mail and credentials otherwise travel in clear
WHEN IT MATTERS Every insecure protocol on this list still exists in the field. Recognising it and naming its replacement is a direct exam objective and a real security finding.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
29

## Slide 30
HIGH-YIELD EXAM FACTS
The Numbers You Must Simply Know
1
Six
Steps in the CompTIA troubleshooting methodology
2
Seven
Stages in the laser imaging process, and steps in malware removal
3
3-2-1
Backup copies, media types, and off-site copies
4
1, 6, 11
The only non-overlapping channels in the 2.4 GHz band
5
100 m
Maximum twisted-pair copper run length
6
4 GB
Maximum file size on a FAT32 volume
7
169.254
The APIPA range that means DHCP failed
8
2
Addresses reserved in every subnet — network and broadcast
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
30

## Slide 31
CONCEPT → PRACTICE → VERIFY
How This Course Is Structured
1
Concepts for the domain
▶
2
Hands-on lab with real tools
▶
3
Verify your own result
▶
4
Recap against the exam objective
▶
5
Practice exam by domain
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
31

## Slide 32
TOPIC 01
Mobile Devices
Laptop hardware · display components · accessories and ports · cellular and wireless · MDM and synchronisation
01
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
32

## Slide 33
CORE 1 · 13% OF CORE 1
Topic 01 at a Glance — Mobile Devices
1
Exam
CompTIA A+ Core 1
2
Domain weighting
13% of Core 1
3
Share of course time
7%
4
Hands-on labs
Lab 1, Lab 2, Lab 3, Lab 4
5
Sub-topics
Laptop hardware · display components · accessories and ports · cellular and wireless · MDM and synchronisation
6
Why it matters
This domain is assessed in both the WSQ Written Assessment and the Practical Performance.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
33

## Slide 34
TOPIC 01 · 13% of Core 1
Key Concepts — Mobile Devices
1
Laptop hardware replacement covers the battery, keyboard and keys, RAM (SODIMM), HDD/SSD migration and replacement, and the wireless cards — each is a field-replaceable unit with its own removal sequence and anti-static precautions.
2
LCD panels do not produce their own light: they need a backlight, historically a CCFL driven by an inverter, and today a strip of LEDs. Flickering or a dim image on an older panel points at the inverter or the backlight rather than the panel itself.
3
LCD panel technologies trade off against each other. TN is fast with poor colour, IPS gives excellent colour and viewing angles, and VA sits between them with the best contrast. OLED needs no backlight at all, giving the deepest blacks and the highest contrast ratio.
4
A digitizer converts analog touch or pen input into digital coordinates. When touch stops working but the image is perfect, the digitizer has failed, not the display panel — on many laptops the two are bonded and replaced as one unit.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
34

## Slide 35
TOPIC 01 · 13% of Core 1
Key Concepts — Mobile Devices (2)
1
Connection methods differ in reach and purpose: USB-C, micro-USB and mini-USB for data and power, Lightning on older Apple devices, NFC for payments within about 4 cm, Bluetooth for peripheral pairing, and hotspot tethering to share a cellular connection.
2
A port replicator reproduces a laptop's existing ports, while a docking station adds capability the laptop never had — full-size drive bays, expansion slots, optical drives and additional display outputs.
3
Cellular generations step up in capability: 2G (GSM and CDMA) carried voice and SMS, 3G added mobile internet and video calling, 4G LTE reached hundreds of megabits per second, and 5G targets multi-gigabit speeds with very low latency.
4
Bluetooth pairing follows a fixed sequence every time — enable Bluetooth, enable pairing mode, discover the device, enter the PIN or confirm the passkey, then test connectivity. Troubleshooting almost always means restarting that sequence.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
35

## Slide 36
TOPIC 01 · 13% of Core 1
Key Concepts — Mobile Devices (3)
1
Mobile device management (MDM) and mobile application management (MAM) let an organisation push corporate email profiles, enforce two-factor authentication, deploy corporate applications and remotely wipe a lost device.
2
Synchronisation binds a device to an account — Microsoft 365, Google Workspace or iCloud — and replicates mail, photos, calendar and contacts. Always check the data cap before enabling a full photo sync over a cellular connection.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
36

## Slide 37
WHAT YOU'LL DO
Hands-On Labs — Mobile Devices
Labs 1–2
• Laptop Teardown and Field-Replaceable Unit Identification
• Mobile Display Technology and Digitizer Fault Diagnosis
Labs 3–4
• Mobile Connectivity — Bluetooth, NFC, Hotspot and Cellular Configuration
• MDM Policy Design and Mobile Synchronisation
—
• —
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
37

## Slide 38
TOPIC 01 · HANDS-ON
Laptop Teardown and Field-Replaceable Unit Identification
LAB 1
Identify and safely replace laptop field-replaceable units — battery, RAM, storage, keyboard and wireless card — with correct ESD precautions (Core 1 objective 1.1).
Working on a training laptop or a high-resolution teardown reference, you identify every field-replaceable unit, record the removal order, and document the anti-static precautions each step requires. You then build a replacement runbook a colleague could follow without supervision.
YOU'LL BUILD
A completed FRU inventory table and a written replacement runbook for one component, with ESD precautions stated at every step.
TOOLCHAIN
Training laptop or teardown reference, anti-static strap and mat, Phillips #00 screwdriver, plastic spudger, parts tray
DONE WHEN
Your FRU inventory lists at least six components with form factor and socket type; the runbook states the internal battery is disconnected first and reconnected last; and the laptop powers on and completes POST after reassembly.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
38

## Slide 39
LAB 1 · PROCESS MAP
How Lab 1 Runs
1
Earth yourself
Anti-static strap clipped to bare chassis metal
2
Fully power down
Shut down, unplug, hold power 15 s to discharge
3
Open the case
Screws into a tray, laid out in chassis order
4
Map every FRU
Battery, RAM, storage, wireless card, keyboard
5
Write the runbook
Numbered steps, tools, ESD notes, verification test
THE POINT
Identify and safely replace laptop field-replaceable units — battery, RAM, storage, keyboard and wireless card — with correct ESD precautions (Core 1 objective 1.1).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
39

## Slide 40
LAB 1 · VERIFY
Laptop Teardown and Field-Replaceable Unit Identification
✅ Expected result
Your FRU inventory lists at least six components with form factor and socket type; the runbook states the internal battery is disconnected first and reconnected last; and the laptop powers on and completes POST after reassembly.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
40

## Slide 41
TOPIC 01 · HANDS-ON
Mobile Display Technology and Digitizer Fault Diagnosis
LAB 2
Compare LCD, IPS, VA and OLED panel technologies and correctly distinguish a display panel fault from a backlight, inverter or digitizer fault (Core 1 objective 1.2).
You compare the four panel technologies on the criteria that matter in support work, then work through a set of display symptoms and decide, for each, which component has actually failed. The output is a diagnostic decision table you can use on the job.
YOU'LL BUILD
A panel technology comparison table and a symptom-to-component diagnostic decision table covering eight display faults.
TOOLCHAIN
Reference displays or specification sheets, a torch, a smartphone with an OLED screen, a laptop with an LCD panel
DONE WHEN
Your decision table covers all eight symptoms with a named component and a confirming test for each, and correctly separates the backlight, inverter, panel and digitizer as four distinct failure points.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
41

## Slide 42
LAB 2 · PROCESS MAP
How Lab 2 Runs
1
Compare the panels
TN, IPS, VA and OLED on colour, angle and contrast
2
Torch test
Prove which panel needs a backlight and which does not
3
Read black level
Full-black image on LCD against OLED, in a dark room
4
Assign the fault
Backlight, inverter, panel or digitizer per symptom
5
Build the table
Eight symptoms, each with a confirming test
THE POINT
Compare LCD, IPS, VA and OLED panel technologies and correctly distinguish a display panel fault from a backlight, inverter or digitizer fault (Core 1 objective 1.2).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
42

## Slide 43
LAB 2 · VERIFY
Mobile Display Technology and Digitizer Fault Diagnosis
✅ Expected result
Your decision table covers all eight symptoms with a named component and a confirming test for each, and correctly separates the backlight, inverter, panel and digitizer as four distinct failure points.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
43

## Slide 44
TOPIC 01 · HANDS-ON
Mobile Connectivity — Bluetooth, NFC, Hotspot and Cellular Configuration
LAB 3
Configure and troubleshoot mobile connection methods including Bluetooth pairing, NFC, hotspot tethering and cellular data settings (Core 1 objectives 1.3 and 1.4).
Using your own mobile device, you work through the full configuration sequence for each connection method, deliberately break each one, and record the symptom and the fix. The output is a connectivity troubleshooting flowchart covering all four methods.
YOU'LL BUILD
A completed configuration log for four connection methods and a troubleshooting flowchart mapping symptoms to fixes.
TOOLCHAIN
Android or iOS device, a second Bluetooth device, a laptop, IP Calculator (https://alfredang.github.io/ipcalculator/)
DONE WHEN
IP Calculator confirms the hotspot address is in a private range with the correct usable host count; your flowchart gives an ordered check sequence for all four symptoms; and each broken-and-fixed cycle is documented with its symptom.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
44

## Slide 45
LAB 3 · PROCESS MAP
How Lab 3 Runs
1
Find the settings
Record the menu path to each connection method
2
Pair over Bluetooth
Enable, discover, PIN, then test that data flows
3
Break and recover
Note the symptom, then which step restored it
4
Share a hotspot
Connect a laptop and record the address it receives
5
Verify the subnet
IP Calculator confirms a private RFC 1918 range
THE POINT
Configure and troubleshoot mobile connection methods including Bluetooth pairing, NFC, hotspot tethering and cellular data settings (Core 1 objectives 1.3 and 1.4).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
45

## Slide 46
LAB 3 · VERIFY
Mobile Connectivity — Bluetooth, NFC, Hotspot and Cellular Configuration
✅ Expected result
IP Calculator confirms the hotspot address is in a private range with the correct usable host count; your flowchart gives an ordered check sequence for all four symptoms; and each broken-and-fixed cycle is documented with its symptom.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
46

## Slide 47
TOPIC 01 · HANDS-ON
MDM Policy Design and Mobile Synchronisation
LAB 4
Design a mobile device management policy and configure account synchronisation for corporate email, calendar and contacts, accounting for data caps (Core 1 objective 1.4).
You design an MDM policy for a small organisation issuing corporate devices, then configure and verify account synchronisation on a real device. You finish by calculating the data cost of a full photo sync so you can advise a user before they exceed their cap.
YOU'LL BUILD
A written MDM policy covering eight control areas, plus a verified synchronisation configuration and a data-cap impact calculation.
TOOLCHAIN
Mobile device, a Microsoft 365 or Google Workspace account, IP Calculator, organisational policy template
DONE WHEN
Your policy covers all eight control areas with a rule and a risk for each, clearly separates MDM from MAM and corporate from BYOD, synchronisation is verified end to end within one minute, and the data-cap calculation supports a stated Wi-Fi-only recommendation.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
47

## Slide 48
LAB 4 · PROCESS MAP
How Lab 4 Runs
1
List the controls
Eight MDM areas from enrolment to remote wipe
2
Write the rules
One rule and one mitigated risk for each area
3
Separate MDM and MAM
Whole device against corporate apps and data only
4
Sync an account
Add the account, then verify in the web client
5
Cost the data
Photo sync against a 5 GB cap; set Wi-Fi only
THE POINT
Design a mobile device management policy and configure account synchronisation for corporate email, calendar and contacts, accounting for data caps (Core 1 objective 1.4).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
48

## Slide 49
LAB 4 · VERIFY
MDM Policy Design and Mobile Synchronisation
✅ Expected result
Your policy covers all eight control areas with a rule and a risk for each, clearly separates MDM from MAM and corporate from BYOD, synchronisation is verified end to end within one minute, and the data-cap calculation supports a stated Wi-Fi-only recommendation.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
49

## Slide 50
TOPIC 01 RECAP · 13% of Core 1
Recap — Mobile Devices
• You can now: Identify and safely replace laptop field-replaceable units — battery, RAM, storage, keyboard and wireless card — with correct ESD precautions (Core 1 objective 1.1).
• You can now: Compare LCD, IPS, VA and OLED panel technologies and correctly distinguish a display panel fault from a backlight, inverter or digitizer fault (Core 1 objective 1.2).
• You can now: Configure and troubleshoot mobile connection methods including Bluetooth pairing, NFC, hotspot tethering and cellular data settings (Core 1 objectives 1.3 and 1.4).
• You can now: Design a mobile device management policy and configure account synchronisation for corporate email, calendar and contacts, accounting for data caps (Core 1 objective 1.4).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
50

## Slide 51
TOPIC 02
Networking
Protocols and ports · network devices · wireless standards · SOHO networks · IP addressing · networking tools
02
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
51

## Slide 52
CORE 1 · 23% OF CORE 1
Topic 02 at a Glance — Networking
1
Exam
CompTIA A+ Core 1
2
Domain weighting
23% of Core 1
3
Share of course time
12%
4
Hands-on labs
Lab 5, Lab 6, Lab 7, Lab 8, Lab 9, Lab 10, Lab 11
5
Sub-topics
Protocols and ports · network devices · wireless standards · SOHO networks · IP addressing · networking tools
6
Why it matters
This domain is assessed in both the WSQ Written Assessment and the Practical Performance.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
52

## Slide 53
TOPIC 02 · 23% of Core 1
Key Concepts — Networking
1
TCP is connection-oriented, sequenced and acknowledged with a 20–60 byte header, so it is used where delivery must be guaranteed. UDP is connectionless with an 8-byte header, so it is used where speed matters more than certainty — DNS queries, streaming and VoIP.
2
The A+ exam tests a fixed list of ports by number: FTP 20/21, SSH and SFTP 22, Telnet 23, SMTP 25, DNS 53, DHCP 67/68, HTTP 80, POP3 110, NetBIOS 137–139, IMAP 143, SNMP 161/162, LDAP 389, HTTPS 443, SMB/CIFS 445 and RDP 3389.
3
Insecure legacy protocols have secure replacements you should be able to name on sight: Telnet gives way to SSH, FTP to SFTP, HTTP to HTTPS, and SNMPv1/v2 to SNMPv3, which is the first version to encrypt its traffic.
4
Network devices sit at different layers. A hub blindly repeats traffic to every port, a switch forwards frames by MAC address, a router forwards packets between broadcast domains by IP address, and a firewall filters traffic by rule.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
53

## Slide 54
TOPIC 02 · 23% of Core 1
Key Concepts — Networking (2)
1
A SOHO router collapses several devices into one box: router, switch, wireless access point, firewall and DHCP server, and often adds content filtering, port forwarding and a VPN endpoint.
2
Power over Ethernet carries both data and electrical power over one Ethernet cable, powering access points, IP cameras and VoIP phones. A PoE switch powers many devices, while a PoE injector powers a single device where no PoE switch exists.
3
The 2.4 GHz band travels further and penetrates walls better but is slower and more congested, offering only three non-overlapping channels — 1, 6 and 11. The 5 GHz band is faster with far more non-overlapping channels but has a shorter usable range.
4
IPv4 addresses are split by a subnet mask into a network portion and a host portion. The number of host bits determines how many usable addresses a subnet provides — always two fewer than the block size, because the network and broadcast addresses are reserved.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
54

## Slide 55
TOPIC 02 · 23% of Core 1
Key Concepts — Networking (3)
1
Private address ranges (10.0.0.0/8, 172.16.0.0/12 and 192.168.0.0/16) are not routable on the internet and must be translated by NAT. An APIPA address in 169.254.0.0/16 means the client asked for DHCP and got no answer.
2
A VPN builds an encrypted tunnel across the public internet so a remote host can reach private LAN resources, while a VLAN partitions one physical switch into several isolated logical networks that each need a router to talk to one another.
3
Networking tools each answer one question: a crimper terminates RJ45 plugs, a cable tester confirms the pinout end to end, a toner probe finds which cable is which in a bundle, a punch-down tool seats wires into a patch panel, a loopback plug proves a port works, and a Wi-Fi analyser shows channel congestion.
4
Common server roles you must recognise are DNS, DHCP, file share, print server, mail server, syslog, web server, proxy, spam gateway, unified threat management appliance and load balancer.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
55

## Slide 56
WHAT YOU'LL DO
Hands-On Labs — Networking
Labs 5–7
• Protocols and Ports — Building the A+ Port Reference
• IPv4 Subnetting and Address Planning with IP Calculator
• Network Devices and Traffic Behaviour Analysis
Labs 8–10
• Wireless Standards, Channel Planning and Interference
• SOHO Network Configuration — DHCP, DNS, NAT and Port Forwarding
• Network Cabling — Termination, Testing and Tool Selection
Lab 11
• Packet Capture Analysis — Reading Real Network Traffic
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
56

## Slide 57
TOPIC 02 · HANDS-ON
Protocols and Ports — Building the A+ Port Reference
LAB 5
Identify the TCP/UDP ports, transport protocol and secure replacement for every protocol on the CompTIA A+ Core 1 objective 2.1 list.
You build the complete A+ port reference table from live evidence rather than memorisation: you query each service on a Killercoda Ubuntu playground, observe which transport it uses, and record the secure alternative where the protocol is insecure. The table becomes your revision sheet.
YOU'LL BUILD
A complete 16-row port reference table with port number, transport, purpose, security status and secure replacement.
TOOLCHAIN
Killercoda Ubuntu Playground (https://killercoda.com/playgrounds/scenario/ubuntu), ss, nmap, /etc/services
DONE WHEN
Your table lists all 16 protocols with the correct port, transport and purpose; every insecure protocol has its secure replacement named; and ss -tulnp output confirms at least one live listening socket with its transport.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
57

## Slide 58
LAB 5 · PROCESS MAP
How Lab 5 Runs
1
Open the playground
A real Ubuntu terminal, root access, in the browser
2
Install the tools
Refresh the package index, then add the net tools
3
Read the port list
Confirm each protocol in the services database
4
Prove the transport
dig shows DNS over UDP; curl confirms HTTP and HTTPS
5
List live sockets
ss -tulnp shows what is listening and on which port
THE POINT
Identify the TCP/UDP ports, transport protocol and secure replacement for every protocol on the CompTIA A+ Core 1 objective 2.1 list.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
58

## Slide 59
LAB 5 · VERIFY
Protocols and Ports — Building the A+ Port Reference
✅ Expected result
Your table lists all 16 protocols with the correct port, transport and purpose; every insecure protocol has its secure replacement named; and ss -tulnp output confirms at least one live listening socket with its transport.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
59

## Slide 60
TOPIC 02 · HANDS-ON
IPv4 Subnetting and Address Planning with IP Calculator
LAB 6
Calculate subnet masks, network and broadcast addresses, usable host ranges and CIDR notation, and design an address plan for a SOHO network (Core 1 objective 2.5).
You use IP Calculator to work subnetting from both directions — decoding a given address and designing a plan to meet a host requirement — then verify every result by hand so you can reproduce it in an exam where no calculator is allowed.
YOU'LL BUILD
A verified subnetting worksheet and a complete four-subnet SOHO address plan exported as CSV.
TOOLCHAIN
IP Calculator (https://alfredang.github.io/ipcalculator/), Killercoda Ubuntu Playground, ipcalc
DONE WHEN
Every subnet in your plan satisfies its host requirement with no wasted block larger than necessary, the hand calculation matches the IP Calculator output for the /26 case, ipcalc agrees with the browser tool, and the CSV export contains all four subnets.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
60

## Slide 61
LAB 6 · PROCESS MAP
How Lab 6 Runs
1
Decode an address
Enter 192.168.10.75/24 and read the full breakdown
2
Change the prefix
Watch network, broadcast and host count change
3
Check it by hand
32 minus 26 gives 6 host bits, 64 block, 62 usable
4
Plan four subnets
Smallest prefix that meets 50, 25, 10 and 5 hosts
5
Export and confirm
Batch to CSV, then cross-check with ipcalc
THE POINT
Calculate subnet masks, network and broadcast addresses, usable host ranges and CIDR notation, and design an address plan for a SOHO network (Core 1 objective 2.5).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
61

## Slide 62
LAB 6 · VERIFY
IPv4 Subnetting and Address Planning with IP Calculator
✅ Expected result
Every subnet in your plan satisfies its host requirement with no wasted block larger than necessary, the hand calculation matches the IP Calculator output for the /26 case, ipcalc agrees with the browser tool, and the CSV export contains all four subnets.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
62

## Slide 63
TOPIC 02 · HANDS-ON
Network Devices and Traffic Behaviour Analysis
LAB 7
Distinguish hub, switch, router, firewall and access point by the layer they operate at and the traffic behaviour each produces (Core 1 objectives 2.2 and 2.3).
Rather than reading device descriptions, you infer device behaviour from captured traffic. Using PCAP Analyzer you examine a capture, identify the MAC and IP conversations, and reason about which device forwarded each frame and why.
YOU'LL BUILD
A device comparison matrix and a written traffic analysis identifying the forwarding decision at each layer.
TOOLCHAIN
PCAP Analyzer (https://alfredang.github.io/pcapanalyzer/), device reference diagrams
DONE WHEN
Your matrix correctly assigns each of the five devices to its OSI layer and forwarding basis; your analysis names the specific MAC and IP addresses observed; and the conclusion is supported by evidence from the capture rather than from theory alone.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
63

## Slide 64
LAB 7 · PROCESS MAP
How Lab 7 Runs
1
Load a capture
Click Sample; parsing happens in your own browser
2
Read the headline
Packets, bytes, duration and average packet size
3
Split by protocol
Record each protocol and its share of the capture
4
Follow the talkers
Top conversations show which pair to investigate
5
Place each device
Hub, switch, router, firewall and AP by OSI layer
THE POINT
Distinguish hub, switch, router, firewall and access point by the layer they operate at and the traffic behaviour each produces (Core 1 objectives 2.2 and 2.3).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
64

## Slide 65
LAB 7 · VERIFY
Network Devices and Traffic Behaviour Analysis
✅ Expected result
Your matrix correctly assigns each of the five devices to its OSI layer and forwarding basis; your analysis names the specific MAC and IP addresses observed; and the conclusion is supported by evidence from the capture rather than from theory alone.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
65

## Slide 66
TOPIC 02 · HANDS-ON
Wireless Standards, Channel Planning and Interference
LAB 8
Compare 802.11 standards and frequency bands, and design a channel plan that avoids co-channel and adjacent-channel interference (Core 1 objective 2.3).
You compare the 2.4 GHz and 5 GHz bands on the criteria that decide real deployments, then design a channel plan for a three-access-point office and justify every channel choice against the non-overlapping channel constraint.
YOU'LL BUILD
An 802.11 standards comparison table and a justified three-AP channel plan with a coverage sketch.
TOOLCHAIN
Wi-Fi analyser application on a mobile device or laptop, 802.11 standards reference, floor plan sketch
DONE WHEN
Your channel plan uses only channels 1, 6 and 11 in the 2.4 GHz band with no adjacent cells sharing a channel; the scan records real SSIDs with channel and dBm; and the justification correctly distinguishes co-channel from adjacent-channel interference.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
66

## Slide 67
LAB 8 · PROCESS MAP
How Lab 8 Runs
1
Table the standards
802.11a through ax on band, speed and width
2
Scan the air
Record every SSID with its channel and dBm
3
Read the strength
-50 excellent, -60 good, -70 usable, -80 unreliable
4
Plan three cells
Assign 1, 6 and 11 so no neighbours share a channel
5
Justify the plan
Separate co-channel from adjacent-channel interference
THE POINT
Compare 802.11 standards and frequency bands, and design a channel plan that avoids co-channel and adjacent-channel interference (Core 1 objective 2.3).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
67

## Slide 68
LAB 8 · VERIFY
Wireless Standards, Channel Planning and Interference
✅ Expected result
Your channel plan uses only channels 1, 6 and 11 in the 2.4 GHz band with no adjacent cells sharing a channel; the scan records real SSIDs with channel and dBm; and the justification correctly distinguishes co-channel from adjacent-channel interference.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
68

## Slide 69
TOPIC 02 · HANDS-ON
SOHO Network Configuration — DHCP, DNS, NAT and Port Forwarding
LAB 9
Configure a SOHO router including DHCP scope, DNS, NAT, DHCP reservations and port forwarding, and verify each service from a client (Core 1 objective 2.5).
You configure the full service set a SOHO router provides, then verify each one from a client using the command line. Where physical hardware is unavailable you use the Killercoda playground to inspect and reason about the same configuration from the client side.
YOU'LL BUILD
A documented SOHO configuration with DHCP scope, reservation, DNS and port-forwarding rule, each verified from a client.
TOOLCHAIN
SOHO router or router emulator, Killercoda Ubuntu Playground, IP Calculator, ipconfig/ip, nslookup/dig
DONE WHEN
The client receives an address inside the DHCP scope and outside the exclusion range, the reservation returns the same address after a release and renew, DNS resolves successfully through the configured resolver, and the port-forwarding rule is documented with its security risk stated.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
69

## Slide 70
LAB 9 · PROCESS MAP
How Lab 9 Runs
1
Plan the addressing
Gateway, static block and DHCP scope before you start
2
Set the DHCP scope
Range, lease and an exclusion for the static block
3
Reserve by MAC
The printer always receives the same address
4
Verify from a client
Release, renew, then read address, gateway and DNS
5
Forward a port
Document the rule and state the security risk
THE POINT
Configure a SOHO router including DHCP scope, DNS, NAT, DHCP reservations and port forwarding, and verify each service from a client (Core 1 objective 2.5).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
70

## Slide 71
LAB 9 · VERIFY
SOHO Network Configuration — DHCP, DNS, NAT and Port Forwarding
✅ Expected result
The client receives an address inside the DHCP scope and outside the exclusion range, the reservation returns the same address after a release and renew, DNS resolves successfully through the configured resolver, and the port-forwarding rule is documented with its security risk stated.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
71

## Slide 72
TOPIC 02 · HANDS-ON
Network Cabling — Termination, Testing and Tool Selection
LAB 10
Terminate twisted-pair cable to T568B, test it end to end, and select the correct tool for each cabling task (Core 1 objectives 2.3 and 3.1).
You terminate a patch cable to the T568B standard, test it with a cable tester, and deliberately create a fault to see how the tester reports it. You then build a tool selection guide matching each networking tool to the single question it answers.
YOU'LL BUILD
A terminated and tested patch cable, a fault-injection test record, and a tool selection guide.
TOOLCHAIN
Crimper, RJ45 plugs, Cat 5e/6 cable, cable stripper, cable tester, toner probe, punch-down tool, loopback plug
DONE WHEN
Your good cable passes the tester with all eight lights in sequence on both ends; the two faulty cables produce distinctly different tester results that you have recorded; and the tool guide matches all seven tools to the specific question each answers.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
72

## Slide 73
LAB 10 · PROCESS MAP
How Lab 10 Runs
1
Recall T568B
Write the eight-wire colour order before you cut
2
Strip and order
25 mm of jacket, conductors flat in T568B order
3
Crimp both ends
Same standard both ends makes a straight-through cable
4
Test the pinout
All eight lights advance in sequence on both units
5
Inject a fault
Swap a pair, then leave one open, and compare results
THE POINT
Terminate twisted-pair cable to T568B, test it end to end, and select the correct tool for each cabling task (Core 1 objectives 2.3 and 3.1).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
73

## Slide 74
LAB 10 · VERIFY
Network Cabling — Termination, Testing and Tool Selection
✅ Expected result
Your good cable passes the tester with all eight lights in sequence on both ends; the two faulty cables produce distinctly different tester results that you have recorded; and the tool guide matches all seven tools to the specific question each answers.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
74

## Slide 75
TOPIC 02 · HANDS-ON
Packet Capture Analysis — Reading Real Network Traffic
LAB 11
Analyse a packet capture to identify protocols, conversations and anomalies, and use the evidence to support a network diagnosis (Core 1 objectives 2.1 and 5.7).
You work a capture the way a support engineer does: start from the summary statistics, narrow by protocol, follow the largest conversation, and read individual packets only once you know which ones matter. The output is a written diagnosis supported by named evidence.
YOU'LL BUILD
A written traffic analysis report with protocol breakdown, conversation analysis and a supported diagnosis.
TOOLCHAIN
PCAP Analyzer (https://alfredang.github.io/pcapanalyzer/), Killercoda Ubuntu Playground, tcpdump
DONE WHEN
tcpdump produces a capture file containing at least three distinct protocols, PCAP Analyzer loads it and reports the protocol distribution, and your written diagnosis cites specific addresses, ports and packet numbers as evidence rather than general statements.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
75

## Slide 76
LAB 11 · PROCESS MAP
How Lab 11 Runs
1
Capture live traffic
tcpdump writes 200 packets to a file on the playground
2
Generate the traffic
curl and a DNS lookup give several protocols to read
3
Load the analyser
Drag the file in, or use Sample if download is blocked
4
Read the mix
Protocol distribution shows what is encrypted and what is not
5
Write the diagnosis
Cite specific addresses, ports and packet numbers
THE POINT
Analyse a packet capture to identify protocols, conversations and anomalies, and use the evidence to support a network diagnosis (Core 1 objectives 2.1 and 5.7).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
76

## Slide 77
LAB 11 · VERIFY
Packet Capture Analysis — Reading Real Network Traffic
✅ Expected result
tcpdump produces a capture file containing at least three distinct protocols, PCAP Analyzer loads it and reports the protocol distribution, and your written diagnosis cites specific addresses, ports and packet numbers as evidence rather than general statements.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
77

## Slide 78
TOPIC 02 RECAP · 23% of Core 1
Recap — Networking
• You can now: Identify the TCP/UDP ports, transport protocol and secure replacement for every protocol on the CompTIA A+ Core 1 objective 2.1 list.
• You can now: Calculate subnet masks, network and broadcast addresses, usable host ranges and CIDR notation, and design an address plan for a SOHO network (Core 1 objective 2.5).
• You can now: Distinguish hub, switch, router, firewall and access point by the layer they operate at and the traffic behaviour each produces (Core 1 objectives 2.2 and 2.3).
• You can now: Compare 802.11 standards and frequency bands, and design a channel plan that avoids co-channel and adjacent-channel interference (Core 1 objective 2.3).
• You can now: Configure a SOHO router including DHCP scope, DNS, NAT, DHCP reservations and port forwarding, and verify each service from a client (Core 1 objective 2.5).
• You can now: Terminate twisted-pair cable to T568B, test it end to end, and select the correct tool for each cabling task (Core 1 objectives 2.3 and 3.1).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
78

## Slide 79
TOPIC 03
Hardware
Cables and connectors · RAM · storage and RAID · motherboards · CPUs and cooling · power supplies · printers
03
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
79

## Slide 80
CORE 1 · 25% OF CORE 1
Topic 03 at a Glance — Hardware
1
Exam
CompTIA A+ Core 1
2
Domain weighting
25% of Core 1
3
Share of course time
13%
4
Hands-on labs
Lab 12, Lab 13, Lab 14, Lab 15, Lab 16, Lab 17, Lab 18
5
Sub-topics
Cables and connectors · RAM · storage and RAID · motherboards · CPUs and cooling · power supplies · printers
6
Why it matters
This domain is assessed in both the WSQ Written Assessment and the Practical Performance.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
80

## Slide 81
TOPIC 03 · 25% of Core 1
Key Concepts — Hardware
1
Copper cable carries electrical signals and is cheap and easy to terminate but is limited to about 100 metres per run and is susceptible to electromagnetic interference. Fibre carries light, is immune to EMI, and reaches tens of kilometres at far higher speeds.
2
Twisted-pair categories set the speed ceiling: Cat 5e carries 1 Gbps, Cat 6 carries 10 Gbps to 55 m, and Cat 6a carries 10 Gbps to the full 100 m. Shielded twisted pair adds a foil or braid screen for use near motors and fluorescent lighting.
3
T568A and T568B are the two RJ45 pinouts. Matching both ends makes a straight-through patch cable; using A at one end and B at the other makes a crossover. Modern switch ports auto-negotiate with Auto-MDIX, so crossover cables are now rare.
4
Display connectors differ in what they can carry. HDMI and DisplayPort carry digital video and audio, DVI carries digital and sometimes analog video only, and VGA is analog only. A passive adapter can change the plug shape but can never convert analog to digital.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
81

## Slide 82
TOPIC 03 · 25% of Core 1
Key Concepts — Hardware (2)
1
RAM comes as DIMMs in desktops and SODIMMs in laptops, and DDR generations are physically keyed so they cannot be mixed. Populating channels in matched pairs enables dual-channel mode and measurably improves memory bandwidth.
2
ECC memory detects and corrects single-bit errors, which makes a server more stable but not faster. It requires a CPU and motherboard that explicitly support it, and it cannot be mixed with non-ECC modules.
3
Storage is chosen on the trade-off between cost and speed. A hard disk drive gives the lowest cost per terabyte but has moving parts, a SATA SSD is far faster with no moving parts, and an NVMe M.2 drive on PCIe lanes is faster still.
4
RAID trades disks for speed or safety. RAID 0 stripes for speed with no redundancy, RAID 1 mirrors for redundancy, RAID 5 stripes with distributed parity and survives one disk failure, and RAID 10 mirrors then stripes for both speed and redundancy.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
82

## Slide 83
TOPIC 03 · 25% of Core 1
Key Concepts — Hardware (3)
1
Motherboard form factors — ATX, micro-ATX, Mini-ITX — set the physical size and how many expansion slots are available. The chipset and CPU socket together decide which processors, memory types and features the board supports.
2
BIOS/UEFI firmware initialises hardware and starts the boot process; CMOS backed by a coin cell stores the settings. A clock that resets to a default date on every boot is the classic sign of a dead CMOS battery.
3
A Trusted Platform Module is a hardware chip that generates and stores cryptographic keys, and it is what BitLocker binds a drive to so the disk cannot simply be moved to another machine and read.
4
A power supply must be sized on total wattage and must supply the right connectors — 24-pin ATX for the board, EPS 4/8-pin for the CPU, PCIe 6/8-pin for the graphics card, and SATA power for drives.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
83

## Slide 84
TOPIC 03 · 25% of Core 1
Key Concepts — Hardware (4)
1
The laser printing process runs in a fixed seven-step order — processing, charging, exposing, developing, transferring, fusing and cleaning — and knowing the order is what lets you turn a print defect into a specific failed component.
2
Printer types suit different jobs: laser for fast, low-cost mono volume, inkjet for affordable colour, impact for multi-part carbon forms, thermal for receipts, and 3D printers using FDM filament or SLA resin for prototyping.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
84

## Slide 85
WHAT YOU'LL DO
Hands-On Labs — Hardware
Labs 12–14
• Cables and Connectors — Identification and Selection
• RAM Identification, Installation and Channel Configuration
• Storage Devices and RAID Level Selection
Labs 15–17
• Motherboard, BIOS/UEFI and CMOS Configuration
• CPU Architecture, Sockets and Cooling Solutions
• Power Supply Sizing, Connectors and Safety
Lab 18
• Printer Installation, Configuration and the Laser Imaging Process
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
85

## Slide 86
TOPIC 03 · HANDS-ON
Cables and Connectors — Identification and Selection
LAB 12
Identify every cable and connector on the A+ objective list by sight and select the correct one for a stated requirement (Core 1 objectives 3.1 and 3.2).
You identify cables and connectors from physical samples or high-resolution references, record the specification that limits each one, and then solve a set of selection scenarios where choosing the wrong cable would fail. The output is a selection guide organised by the question it answers.
YOU'LL BUILD
A completed cable and connector identification table and a solved set of eight selection scenarios.
TOOLCHAIN
Cable and connector samples or reference images, specification sheets, measuring tape
DONE WHEN
Your identification table covers at least 20 connectors with speed and distance limits; every scenario answer names a specific cable or connector and justifies it against a stated limit rather than a preference.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
86

## Slide 87
LAB 12 · PROCESS MAP
How Lab 12 Runs
1
Table the connectors
Name, media, speed, distance and typical use
2
Group by purpose
Network, video, peripheral and storage families
3
Record the limits
Cat 5e 1 Gbps, Cat 6a 10 Gbps to a 100 m maximum
4
Solve the scenarios
120 m run, EMI-heavy route, analog to digital
5
Build the guide
Organised by how far, how fast, and does it carry power
THE POINT
Identify every cable and connector on the A+ objective list by sight and select the correct one for a stated requirement (Core 1 objectives 3.1 and 3.2).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
87

## Slide 88
LAB 12 · VERIFY
Cables and Connectors — Identification and Selection
✅ Expected result
Your identification table covers at least 20 connectors with speed and distance limits; every scenario answer names a specific cable or connector and justifies it against a stated limit rather than a preference.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
88

## Slide 89
TOPIC 03 · HANDS-ON
RAM Identification, Installation and Channel Configuration
LAB 13
Identify RAM types and form factors, install modules correctly and configure dual-channel operation, verifying the result in firmware and the OS (Core 1 objective 3.3).
You identify memory by its physical keying and label, install modules into the correct slots for dual-channel operation, and then verify from both firmware and the operating system that the configuration took effect. You also read a module label the way a technician ordering a replacement must.
YOU'LL BUILD
A RAM specification decode, a verified dual-channel installation and a memory upgrade recommendation for a stated workload.
TOOLCHAIN
Training PC or laptop, DIMM and SODIMM modules, anti-static strap, Task Manager, CPU-Z or equivalent
DONE WHEN
The system POSTs and reports the full installed capacity, Task Manager confirms the correct speed and slot usage, dual channel is confirmed in firmware, and your upgrade recommendation names a specific module that the chipset actually supports.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
89

## Slide 90
LAB 13 · PROCESS MAP
How Lab 13 Runs
1
Earth and open
Strap on, power removed, discharge before touching RAM
2
Read the label
Capacity, DDR generation, speed, CAS latency and ECC
3
Check the key
The notch proves DDR3, DDR4 and DDR5 cannot be mixed
4
Fill the channel pair
Matched modules in the colour-matched slots
5
Verify in firmware
BIOS and Task Manager confirm speed and dual channel
THE POINT
Identify RAM types and form factors, install modules correctly and configure dual-channel operation, verifying the result in firmware and the OS (Core 1 objective 3.3).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
90

## Slide 91
LAB 13 · VERIFY
RAM Identification, Installation and Channel Configuration
✅ Expected result
The system POSTs and reports the full installed capacity, Task Manager confirms the correct speed and slot usage, dual channel is confirmed in firmware, and your upgrade recommendation names a specific module that the chipset actually supports.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
91

## Slide 92
TOPIC 03 · HANDS-ON
Storage Devices and RAID Level Selection
LAB 14
Compare HDD, SSD, NVMe and hybrid storage, and select the correct RAID level for a stated capacity, performance and redundancy requirement (Core 1 objectives 3.3 and 3.4).
You compare storage technologies on the trade-offs that decide real purchases, then work a set of RAID selection scenarios where the wrong level means either lost data or wasted money. You finish by calculating usable capacity and fault tolerance for each level.
YOU'LL BUILD
A storage comparison table, a RAID capacity and fault-tolerance calculation sheet, and four justified RAID selections.
TOOLCHAIN
Storage device samples or references, Killercoda Ubuntu Playground, lsblk, RAID reference diagrams
DONE WHEN
Your capacity calculations for four 2 TB disks are correct for all four RAID levels, every scenario selection is justified against the stated requirement, and the comparison table correctly ranks the four storage types on speed and cost per terabyte.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
92

## Slide 93
LAB 14 · PROCESS MAP
How Lab 14 Runs
1
Compare the media
HDD, SATA SSD, NVMe and SSHD on speed and cost
2
Explain the interface
NVMe runs on PCIe lanes, not the SATA controller
3
Inspect the devices
lsblk and df show size, type and free capacity
4
Calculate the RAID
Four 2 TB disks give 8, 4, 6 and 4 TB usable
5
Select for the case
Match level to capacity, speed and fault tolerance
THE POINT
Compare HDD, SSD, NVMe and hybrid storage, and select the correct RAID level for a stated capacity, performance and redundancy requirement (Core 1 objectives 3.3 and 3.4).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
93

## Slide 94
LAB 14 · VERIFY
Storage Devices and RAID Level Selection
✅ Expected result
Your capacity calculations for four 2 TB disks are correct for all four RAID levels, every scenario selection is justified against the stated requirement, and the comparison table correctly ranks the four storage types on speed and cost per terabyte.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
94

## Slide 95
TOPIC 03 · HANDS-ON
Motherboard, BIOS/UEFI and CMOS Configuration
LAB 15
Identify motherboard form factors, expansion slots and headers, and configure BIOS/UEFI settings including boot order, virtualization support, Secure Boot and TPM (Core 1 objectives 3.4 and 3.5).
You map a motherboard component by component, then enter firmware and configure the settings that matter in support work — boot order, virtualization support, Secure Boot and the TPM — recording where each lives so you can find it again on an unfamiliar board.
YOU'LL BUILD
An annotated motherboard map and a documented BIOS/UEFI configuration record with the menu path for each setting.
TOOLCHAIN
Training PC, motherboard reference or physical board, BIOS/UEFI setup utility, msinfo32
DONE WHEN
msinfo32 reports the expected BIOS mode and Secure Boot state, virtualization support is enabled and confirmed, and your configuration record gives the exact menu path for boot order, virtualization, Secure Boot and TPM.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
95

## Slide 96
LAB 15 · PROCESS MAP
How Lab 15 Runs
1
Identify the board
Form factor from its dimensions and mounting holes
2
Label the sockets
CPU socket, memory slots, PCIe slots and M.2
3
Find the power inputs
24-pin ATX and the EPS connector for the CPU
4
Enter the firmware
Record the key, then the boot order menu path
5
Enable and verify
Virtualization, Secure Boot and TPM, confirmed in msinfo32
THE POINT
Identify motherboard form factors, expansion slots and headers, and configure BIOS/UEFI settings including boot order, virtualization support, Secure Boot and TPM (Core 1 objectives 3.4 and 3.5).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
96

## Slide 97
LAB 15 · VERIFY
Motherboard, BIOS/UEFI and CMOS Configuration
✅ Expected result
msinfo32 reports the expected BIOS mode and Secure Boot state, virtualization support is enabled and confirmed, and your configuration record gives the exact menu path for boot order, virtualization, Secure Boot and TPM.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
97

## Slide 98
TOPIC 03 · HANDS-ON
CPU Architecture, Sockets and Cooling Solutions
LAB 16
Compare CPU architectures, socket types and cooling solutions, and diagnose thermal problems from observed behaviour (Core 1 objectives 3.4 and 5.2).
You compare x86-64 and ARM on the criteria that decide platform choice, match processors to sockets, and then work the thermal chain from paste to airflow — because most CPU problems in the field are thermal rather than electrical.
YOU'LL BUILD
A CPU and socket compatibility matrix, a cooling comparison, and a thermal fault diagnostic sequence.
TOOLCHAIN
Training PC, CPU and cooler samples or references, thermal paste, Task Manager, hardware monitoring utility
DONE WHEN
Task Manager confirms the core and logical processor counts and the virtualization state; your diagnostic sequence orders the checks from cheapest to most invasive; and the temperature record supports a stated conclusion about cooling adequacy.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
98

## Slide 99
LAB 16 · PROCESS MAP
How Lab 16 Runs
1
Compare architectures
x86-64 against ARM on power, heat and compatibility
2
Match socket types
LGA, PGA and soldered BGA in mobile devices
3
Read the CPU
Cores, logical processors, speed and virtualization state
4
Explain throttling
Clock drops to protect the silicon when it runs too hot
5
Diagnose the thermals
Fans, dust, seating, paste, then ambient airflow
THE POINT
Compare CPU architectures, socket types and cooling solutions, and diagnose thermal problems from observed behaviour (Core 1 objectives 3.4 and 5.2).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
99

## Slide 100
LAB 16 · VERIFY
CPU Architecture, Sockets and Cooling Solutions
✅ Expected result
Task Manager confirms the core and logical processor counts and the virtualization state; your diagnostic sequence orders the checks from cheapest to most invasive; and the temperature record supports a stated conclusion about cooling adequacy.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
100

## Slide 101
TOPIC 03 · HANDS-ON
Power Supply Sizing, Connectors and Safety
LAB 17
Select a power supply by wattage, form factor, efficiency and connector complement, and apply electrical safety rules when working with power (Core 1 objectives 3.5 and 4.5).
You calculate the wattage a build actually requires, select a supply with the right connectors and headroom, and record the safety rules that apply. The safety section is not optional background — a power supply retains a lethal charge after disconnection.
YOU'LL BUILD
A power budget calculation, a justified PSU selection with connector checklist, and a written electrical safety procedure.
TOOLCHAIN
PSU samples or specification sheets, PSU wattage calculator, training PC, multimeter (demonstration only)
DONE WHEN
Your power budget sums every component and adds stated headroom, the selected supply provides every connector the build requires, and the safety procedure explicitly forbids opening the PSU and requires discharge before internal work.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
101

## Slide 102
LAB 17 · PROCESS MAP
How Lab 17 Runs
1
State the safety rule
Never open a PSU — its capacitors hold a lethal charge
2
Budget the wattage
Sum peak draw, then add 30 percent headroom
3
List the connectors
24-pin, EPS, PCIe and SATA power for every device
4
Match form and tier
ATX or SFX to the case; 80 PLUS efficiency tier
5
Justify the choice
Wattage defended against the calculated budget
THE POINT
Select a power supply by wattage, form factor, efficiency and connector complement, and apply electrical safety rules when working with power (Core 1 objectives 3.5 and 4.5).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
102

## Slide 103
LAB 17 · VERIFY
Power Supply Sizing, Connectors and Safety
✅ Expected result
Your power budget sums every component and adds stated headroom, the selected supply provides every connector the build requires, and the safety procedure explicitly forbids opening the PSU and requires discharge before internal work.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
103

## Slide 104
TOPIC 03 · HANDS-ON
Printer Installation, Configuration and the Laser Imaging Process
LAB 18
Install and share a printer, configure its settings and security, and map each stage of the laser imaging process to the print defect its failure produces (Core 1 objectives 3.6 and 3.7).
You install and share a printer, configure the settings users actually ask about, then learn the seven-step laser process in order — because knowing the order is exactly what converts a print defect into a named failed component.
YOU'LL BUILD
A configured and shared printer, a printer settings reference, and a laser process defect map linking each stage to its symptom.
TOOLCHAIN
Printer or printer emulator, Windows print management, laser printer reference diagram, PCL/PostScript drivers
DONE WHEN
The printer prints a test page and is shared successfully, your defect map correctly links at least four print defects to the specific laser stage that failed, and the safety rules include the toner vacuum and hot fuser warnings.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
104

## Slide 105
LAB 18 · PROCESS MAP
How Lab 18 Runs
1
Site and connect
Clearance, power and the right data connection
2
Install the driver
PCL or PostScript, then print a test page
3
Configure and share
Duplex, tray, quality, then sharing and security
4
Learn the seven stages
Process, charge, expose, develop, transfer, fuse, clean
5
Map defect to stage
Lines to the drum, smudging to the fuser, ghosting to cleaning
THE POINT
Install and share a printer, configure its settings and security, and map each stage of the laser imaging process to the print defect its failure produces (Core 1 objectives 3.6 and 3.7).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
105

## Slide 106
LAB 18 · VERIFY
Printer Installation, Configuration and the Laser Imaging Process
✅ Expected result
The printer prints a test page and is shared successfully, your defect map correctly links at least four print defects to the specific laser stage that failed, and the safety rules include the toner vacuum and hot fuser warnings.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
106

## Slide 107
TOPIC 03 RECAP · 25% of Core 1
Recap — Hardware
• You can now: Identify every cable and connector on the A+ objective list by sight and select the correct one for a stated requirement (Core 1 objectives 3.1 and 3.2).
• You can now: Identify RAM types and form factors, install modules correctly and configure dual-channel operation, verifying the result in firmware and the OS (Core 1 objective 3.3).
• You can now: Compare HDD, SSD, NVMe and hybrid storage, and select the correct RAID level for a stated capacity, performance and redundancy requirement (Core 1 objectives 3.3 and 3.4).
• You can now: Identify motherboard form factors, expansion slots and headers, and configure BIOS/UEFI settings including boot order, virtualization support, Secure Boot and TPM (Core 1 objectives 3.4 and 3.5).
• You can now: Compare CPU architectures, socket types and cooling solutions, and diagnose thermal problems from observed behaviour (Core 1 objectives 3.4 and 5.2).
• You can now: Select a power supply by wattage, form factor, efficiency and connector complement, and apply electrical safety rules when working with power (Core 1 objectives 3.5 and 4.5).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
107

## Slide 108
TOPIC 04
Virtualization and Cloud Computing
Hypervisors · virtual machines · resource requirements · cloud models · shared resources and metered use
04
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
108

## Slide 109
CORE 1 · 11% OF CORE 1
Topic 04 at a Glance — Virtualization and Cloud Computing
1
Exam
CompTIA A+ Core 1
2
Domain weighting
11% of Core 1
3
Share of course time
6%
4
Hands-on labs
Lab 19, Lab 20, Lab 21
5
Sub-topics
Hypervisors · virtual machines · resource requirements · cloud models · shared resources and metered use
6
Why it matters
This domain is assessed in both the WSQ Written Assessment and the Practical Performance.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
109

## Slide 110
TOPIC 04 · 11% of Core 1
Key Concepts — Virtualization and Cloud Computing
1
Virtualization runs several operating systems on one physical machine through a hypervisor, cutting hardware cost, power and rack space while letting you snapshot and roll back a whole machine in seconds.
2
A Type 1 (bare-metal) hypervisor such as ESXi or Hyper-V runs directly on the hardware and is used in data centres. A Type 2 (hosted) hypervisor such as VirtualBox or VMware Workstation runs as an application on top of a desktop OS.
3
Each virtual machine needs the same resources a physical machine would — its own vCPU allocation, RAM, disk and network adapter. Over-committing RAM across many VMs is the most common cause of a host grinding to a halt.
4
Hardware virtualization support (Intel VT-x or AMD-V) must be enabled in BIOS/UEFI before a 64-bit guest will start. A hypervisor refusing to launch a VM is very often this setting rather than a software fault.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
110

## Slide 111
TOPIC 04 · 11% of Core 1
Key Concepts — Virtualization and Cloud Computing (2)
1
Virtual desktop infrastructure hosts user desktops centrally and streams them to thin clients, which simplifies patching and secures data by keeping it in the data centre rather than on the endpoint.
2
Cloud characteristics that define the model are shared resources, rapid elasticity, high availability, file synchronisation and metered utilisation — you pay for what you consume rather than for the capacity you provisioned.
3
Deployment models describe who owns the infrastructure: public cloud is shared multi-tenant, private cloud is dedicated to one organisation, community cloud is shared by organisations with common requirements, and hybrid cloud spans private and public.
4
Service models describe how much you manage. With IaaS you manage the OS and everything above it, with PaaS you manage only your application and data, and with SaaS the provider manages everything and you simply use the software.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
111

## Slide 112
WHAT YOU'LL DO
Hands-On Labs — Virtualization and Cloud Computing
Lab 19
• Hypervisor Types and Virtual Machine Resource Planning
Lab 20
• Building and Configuring a Linux Virtual Machine
Lab 21
• Cloud Service and Deployment Model Selection
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
112

## Slide 113
TOPIC 04 · HANDS-ON
Hypervisor Types and Virtual Machine Resource Planning
LAB 19
Distinguish Type 1 from Type 2 hypervisors, plan virtual machine resource allocation and identify the firmware prerequisite for virtualization (Core 1 objective 4.2).
You compare the two hypervisor types on where they run and what they are for, verify that hardware virtualization support is enabled, then plan resource allocation for several VMs on one host — the calculation that decides whether a host performs or crawls.
YOU'LL BUILD
A hypervisor comparison table, a verified virtualization-enabled host and a resource allocation plan for four VMs.
TOOLCHAIN
Windows host, Task Manager, systeminfo, BIOS/UEFI, VirtualBox or Hyper-V, hypervisor references
DONE WHEN
Virtualization support is confirmed enabled on the host, your allocation plan's total RAM leaves at least 4 GB for the host, and every VM is allocated at or above its guest OS minimum with the margin stated.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
113

## Slide 114
LAB 19 · PROCESS MAP
How Lab 19 Runs
1
Separate the types
Type 1 on bare metal, Type 2 on a host OS
2
Explain the overhead
No host OS means no competing scheduler
3
Check the firmware
VT-x or AMD-V must be on or no 64-bit guest starts
4
Measure the host
Cores, total RAM and free disk before allocating
5
Allocate and check
Leave at least 4 GB for the host after all four VMs
THE POINT
Distinguish Type 1 from Type 2 hypervisors, plan virtual machine resource allocation and identify the firmware prerequisite for virtualization (Core 1 objective 4.2).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
114

## Slide 115
LAB 19 · VERIFY
Hypervisor Types and Virtual Machine Resource Planning
✅ Expected result
Virtualization support is confirmed enabled on the host, your allocation plan's total RAM leaves at least 4 GB for the host, and every VM is allocated at or above its guest OS minimum with the margin stated.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
115

## Slide 116
TOPIC 04 · HANDS-ON
Building and Configuring a Linux Virtual Machine
LAB 20
Provision, configure and verify a Linux virtual machine, and perform the post-installation tasks a technician must complete on any new guest (Core 1 objective 4.2).
You provision a working Linux environment and complete the full post-installation checklist — updates, networking, users, storage and a snapshot — using the Killercoda Ubuntu playground so that no local install or licence is required and every learner gets an identical environment.
YOU'LL BUILD
A configured Linux environment with verified networking, a created user, installed packages and a documented build record.
TOOLCHAIN
Killercoda Ubuntu Playground (https://killercoda.com/playgrounds/scenario/ubuntu)
DONE WHEN
The OS version and resources are recorded, updates complete without error, ping and dig both succeed, the aplus user exists in the sudo group, and the labs directory tree is owned by aplus rather than root.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
116

## Slide 117
LAB 20 · PROCESS MAP
How Lab 20 Runs
1
Open the playground
A real Ubuntu machine with root, in a browser tab
2
Identify the guest
Distribution, version, kernel and architecture
3
Patch and install
Update the index, upgrade, then add the tool set
4
Verify the network
Addresses, default route, resolvers, ping and dig
5
Create a user
Standard account plus sudo, owning its own directories
THE POINT
Provision, configure and verify a Linux virtual machine, and perform the post-installation tasks a technician must complete on any new guest (Core 1 objective 4.2).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
117

## Slide 118
LAB 20 · VERIFY
Building and Configuring a Linux Virtual Machine
✅ Expected result
The OS version and resources are recorded, updates complete without error, ping and dig both succeed, the aplus user exists in the sudo group, and the labs directory tree is owned by aplus rather than root.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
118

## Slide 119
TOPIC 04 · HANDS-ON
Cloud Service and Deployment Model Selection
LAB 21
Compare IaaS, PaaS and SaaS and the public, private, community and hybrid deployment models, and select the correct combination for a stated business requirement (Core 1 objective 4.1).
You build the responsibility matrix that separates the three service models, compare the four deployment models on the concerns that decide them, and then solve selection scenarios where the wrong choice creates either a compliance breach or an unnecessary cost.
YOU'LL BUILD
A shared-responsibility matrix, a deployment model comparison and six justified service and deployment selections.
TOOLCHAIN
Cloud provider documentation, IaaS/PaaS/SaaS reference material, organisational scenario briefs
DONE WHEN
Your responsibility matrix correctly divides all nine layers across on-premises, IaaS, PaaS and SaaS; every scenario names both a service model and a deployment model; and each justification cites the specific requirement that ruled the alternatives out.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
119

## Slide 120
LAB 21 · PROCESS MAP
How Lab 21 Runs
1
Build the matrix
Nine layers across on-premises, IaaS, PaaS and SaaS
2
Place the boundary
Who manages the OS, the runtime and the application
3
Compare deployments
Public, private, community and hybrid on control and cost
4
Recall the traits
Shared, elastic, available, synchronised and metered
5
Select per scenario
Name both a service and a deployment model, and justify
THE POINT
Compare IaaS, PaaS and SaaS and the public, private, community and hybrid deployment models, and select the correct combination for a stated business requirement (Core 1 objective 4.1).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
120

## Slide 121
LAB 21 · VERIFY
Cloud Service and Deployment Model Selection
✅ Expected result
Your responsibility matrix correctly divides all nine layers across on-premises, IaaS, PaaS and SaaS; every scenario names both a service model and a deployment model; and each justification cites the specific requirement that ruled the alternatives out.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
121

## Slide 122
TOPIC 04 RECAP · 11% of Core 1
Recap — Virtualization and Cloud Computing
• You can now: Distinguish Type 1 from Type 2 hypervisors, plan virtual machine resource allocation and identify the firmware prerequisite for virtualization (Core 1 objective 4.2).
• You can now: Provision, configure and verify a Linux virtual machine, and perform the post-installation tasks a technician must complete on any new guest (Core 1 objective 4.2).
• You can now: Compare IaaS, PaaS and SaaS and the public, private, community and hybrid deployment models, and select the correct combination for a stated business requirement (Core 1 objective 4.1).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
122

## Slide 123
TOPIC 05
Hardware and Network Troubleshooting
The CompTIA troubleshooting methodology · POST and boot faults · storage and RAID · display faults · printer and network symptoms
05
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
123

## Slide 124
CORE 1 · 28% OF CORE 1
Topic 05 at a Glance — Hardware and Network Troubleshooting
1
Exam
CompTIA A+ Core 1
2
Domain weighting
28% of Core 1
3
Share of course time
15%
4
Hands-on labs
Lab 22, Lab 23, Lab 24, Lab 25, Lab 26, Lab 27, Lab 28
5
Sub-topics
The CompTIA troubleshooting methodology · POST and boot faults · storage and RAID · display faults · printer and network symptoms
6
Why it matters
This domain is assessed in both the WSQ Written Assessment and the Practical Performance.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
124

## Slide 125
TOPIC 05 · 28% of Core 1
Key Concepts — Hardware and Network Troubleshooting
1
The CompTIA six-step methodology is examinable in order: identify the problem, establish a theory of probable cause, test the theory to determine the cause, establish a plan of action and implement the solution, verify full system functionality and implement preventive measures, then document findings, actions and outcomes.
2
Always question the obvious first and ask what changed. Most faults in the field are a recent change — a new driver, a moved cable, an installed update — rather than a spontaneous hardware failure.
3
When a theory is not confirmed, you establish a new theory or escalate. Escalation is a legitimate step in the methodology, not an admission of failure, and it belongs in the documentation.
4
POST beep codes and diagnostic LEDs report faults before any video output exists. A repeating beep pattern usually indicates RAM or graphics, and reseating the module is the correct first action.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
125

## Slide 126
TOPIC 05 · 28% of Core 1
Key Concepts — Hardware and Network Troubleshooting (2)
1
A blue screen of death or a macOS pinwheel points at a driver, failing RAM or a failing disk. Read the stop code, note what changed immediately before it, and test memory before replacing anything.
2
Symptom clusters point at causes: a burning smell means shut down and unplug immediately, a grinding noise means a failing fan or drive, capacitor swelling means the motherboard is finished, and a date that resets each boot means the CMOS battery is dead.
3
Overheating shows as thermal throttling, random reboots or shutdown under load. Check that fans spin, that intakes and heatsink fins are free of dust, that ambient airflow is adequate, and that thermal paste has not dried out.
4
S.M.A.R.T. reports a drive's own health data — reallocated sectors, pending sectors and read error rate. A S.M.A.R.T. warning means back up the data now and replace the drive; it does not mean you have time.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
126

## Slide 127
TOPIC 05 · 28% of Core 1
Key Concepts — Hardware and Network Troubleshooting (3)
1
RAID recovery depends on the level. RAID 1, 5 and 10 survive a single disk failure and rebuild after you replace the drive, but RAID 0 has no redundancy at all and any single failure means restoring from backup.
2
Display faults follow a short checklist: wrong input source, a physical cable fault, a dead backlight or projector bulb producing a dim image, burn-in from a static image, dead pixels, and colour problems from a wrong or damaged cable.
3
Print defects map to components in the laser process — vertical lines mean a scratched drum, garbled output means the wrong driver, toner that wipes off means the fuser has failed, and repeated ghost images mean the drum is not being cleaned.
4
Network symptoms have distinct signatures: an APIPA address means DHCP failed, high latency and jitter degrade VoIP and need QoS, port flapping points at a physical cable or connector fault, and intermittent wireless usually means distance, interference or channel overlap.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
127

## Slide 128
WHAT YOU'LL DO
Hands-On Labs — Hardware and Network Troubleshooting
Labs 22–24
• Applying the CompTIA Six-Step Troubleshooting Methodology
• POST, Boot and Power Fault Diagnosis
• Storage and RAID Fault Diagnosis with S.M.A.R.T.
Labs 25–27
• Display and Projector Fault Diagnosis
• Mobile Device Hardware Fault Diagnosis
• Printer Fault Diagnosis from Print Defects
Lab 28
• Network Fault Diagnosis — Command Line to Packet Level
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
128

## Slide 129
TOPIC 05 · HANDS-ON
Applying the CompTIA Six-Step Troubleshooting Methodology
LAB 22
Apply the CompTIA six-step troubleshooting methodology in order to a real fault, documenting each step (Core 1 objective 5.1).
The methodology is examinable in order and is the framework every other troubleshooting lab in this course hangs from. You apply all six steps to a fault, writing the evidence at each step, and produce the documentation that step six actually requires.
YOU'LL BUILD
A completed six-step troubleshooting record for one fault, with evidence and a preventive measure at each step.
TOOLCHAIN
Training PC with an injected fault, ticketing template, Killercoda Ubuntu Playground
DONE WHEN
Your record contains all six steps in the correct order, each with written evidence; a rollback position is stated before implementation; a specific preventive measure is named; and the DNS exercise shows the fault reproduced and then resolved.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
129

## Slide 130
LAB 22 · PROCESS MAP
How Lab 22 Runs
1
Learn the six steps
Identify, theorise, test, plan, verify, then document
2
Interview and back up
Ask what changed, and protect the data first
3
Design a real test
One that would disprove the theory if it were wrong
4
Plan with a rollback
State the way back before you change anything
5
Verify and document
Prove the fix, prevent recurrence, write it up
THE POINT
Apply the CompTIA six-step troubleshooting methodology in order to a real fault, documenting each step (Core 1 objective 5.1).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
130

## Slide 131
LAB 22 · VERIFY
Applying the CompTIA Six-Step Troubleshooting Methodology
✅ Expected result
Your record contains all six steps in the correct order, each with written evidence; a rollback position is stated before implementation; a specific preventive measure is named; and the DNS exercise shows the fault reproduced and then resolved.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
131

## Slide 132
TOPIC 05 · HANDS-ON
POST, Boot and Power Fault Diagnosis
LAB 23
Diagnose no-power, no-POST and no-boot faults using beep codes, diagnostic LEDs and a systematic elimination sequence (Core 1 objective 5.2).
A machine that will not start gives you almost no information, so you need a fixed elimination sequence rather than guesswork. You build that sequence, learn to read the signals the board does give — beep codes and LEDs — and separate the three distinct failure classes.
YOU'LL BUILD
A three-branch diagnostic flowchart for no-power, no-POST and no-boot, plus a beep code and LED reference.
TOOLCHAIN
Training PC, motherboard manual, POST diagnostic references, PSU tester or multimeter
DONE WHEN
Your flowchart routes to the correct branch from the entry symptom in no more than two questions, each branch orders its checks from cheapest and least invasive to most, and the minimum configuration test is included in the no-POST branch.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
132

## Slide 133
LAB 23 · PROCESS MAP
How Lab 23 Runs
1
Classify the failure
No power, no POST, or POST completes but no boot
2
Work the power branch
Socket, lead, switch, PSU, then the board itself
3
Read what it tells you
Beep codes and diagnostic LEDs before any teardown
4
Reseat and strip back
RAM and graphics, then the minimum configuration
5
Fix the boot path
Boot order, stray USB, disk detection, boot record
THE POINT
Diagnose no-power, no-POST and no-boot faults using beep codes, diagnostic LEDs and a systematic elimination sequence (Core 1 objective 5.2).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
133

## Slide 134
LAB 23 · VERIFY
POST, Boot and Power Fault Diagnosis
✅ Expected result
Your flowchart routes to the correct branch from the entry symptom in no more than two questions, each branch orders its checks from cheapest and least invasive to most, and the minimum configuration test is included in the no-POST branch.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
134

## Slide 135
TOPIC 05 · HANDS-ON
Storage and RAID Fault Diagnosis with S.M.A.R.T.
LAB 24
Diagnose storage faults using S.M.A.R.T. data, symptom analysis and RAID status, and choose the correct recovery action for each RAID level (Core 1 objective 5.3).
Storage faults are the ones where a wrong move destroys the data permanently, so the order of actions matters more than in any other troubleshooting lab. You read S.M.A.R.T. attributes, interpret the warning signs, and decide the recovery action per RAID level.
YOU'LL BUILD
A S.M.A.R.T. attribute interpretation record, a storage symptom map and a RAID recovery decision table.
TOOLCHAIN
Training PC, Killercoda Ubuntu Playground, smartctl, chkdsk, Disk Management, wmic
DONE WHEN
Your record names at least four S.M.A.R.T. attributes and states the correct action for a non-zero reallocated sector count; the recovery table gives a distinct action for all four RAID levels; and the rebuild risk is stated explicitly.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
135

## Slide 136
LAB 24 · PROCESS MAP
How Lab 24 Runs
1
Protect the data first
Back up before diagnostics — they can finish a dying drive
2
Check the health
wmic and Disk Management report status and capacity
3
Read S.M.A.R.T.
Reallocated, pending and uncorrectable sector counts
4
Act on the warning
Any non-zero count means back up now and replace
5
Recover the array
RAID 1, 5 and 10 rebuild; RAID 0 means restore
THE POINT
Diagnose storage faults using S.M.A.R.T. data, symptom analysis and RAID status, and choose the correct recovery action for each RAID level (Core 1 objective 5.3).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
136

## Slide 137
LAB 24 · VERIFY
Storage and RAID Fault Diagnosis with S.M.A.R.T.
✅ Expected result
Your record names at least four S.M.A.R.T. attributes and states the correct action for a non-zero reallocated sector count; the recovery table gives a distinct action for all four RAID levels; and the rebuild risk is stated explicitly.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
137

## Slide 138
TOPIC 05 · HANDS-ON
Display and Projector Fault Diagnosis
LAB 25
Diagnose display and projector faults by isolating source, cable, panel, backlight and settings as distinct failure points (Core 1 objective 5.4).
Display faults are frequently misdiagnosed as a dead monitor when the real cause is a wrong input, a failing cable or a dead backlight. You build the isolation sequence that identifies which of the five components has actually failed before any part is ordered.
YOU'LL BUILD
A display fault isolation sequence and a symptom-to-cause map covering twelve display and projector faults.
TOOLCHAIN
Monitor, projector, spare display cables, training PC, torch, display settings
DONE WHEN
Your isolation sequence checks input selection before substituting any hardware, the map covers all twelve faults with a named component and a confirming test, and the backlight, panel and signal path are treated as three separate failure points.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
138

## Slide 139
LAB 25 · PROCESS MAP
How Lab 25 Runs
1
Check the source
Confirm the machine is on and producing output
2
Check the input
A wrong input selection is the commonest complaint
3
Substitute the cable
A cable can fail intermittently while looking intact
4
Isolate the backlight
A faint image under a torch means backlight or inverter
5
Map the rest
Burn-in, dead pixels, colour, dim bulb and shutdown
THE POINT
Diagnose display and projector faults by isolating source, cable, panel, backlight and settings as distinct failure points (Core 1 objective 5.4).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
139

## Slide 140
LAB 25 · VERIFY
Display and Projector Fault Diagnosis
✅ Expected result
Your isolation sequence checks input selection before substituting any hardware, the map covers all twelve faults with a named component and a confirming test, and the backlight, panel and signal path are treated as three separate failure points.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
140

## Slide 141
TOPIC 05 · HANDS-ON
Mobile Device Hardware Fault Diagnosis
LAB 26
Diagnose mobile device hardware faults including battery, charging, screen, digitizer, port and overheating problems, applying the correct safety response (Core 1 objective 5.5).
Mobile faults carry a safety dimension that desktop faults do not: a swollen lithium battery is a fire and chemical hazard. You build the diagnostic map and, for each fault, record both the technical response and the safety response.
YOU'LL BUILD
A mobile fault diagnostic map with a technical and a safety response for each of ten faults.
TOOLCHAIN
Mobile device, charging cables, battery health screens, device settings
DONE WHEN
Every fault in your map has both a technical and a safety response; the swollen battery entry forbids puncturing, compressing and charging; and the charging diagnosis substitutes cable and charger before the battery is suspected.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
141

## Slide 142
LAB 26 · PROCESS MAP
How Lab 26 Runs
1
State the safety rule
Never puncture, compress or charge a swollen battery
2
Read the battery
Maximum capacity and cycle count from device settings
3
Split the causes
Degraded cell, background apps, weak signal or brightness
4
Test the charge path
Cable, then charger, then the port, then the battery
5
Separate screen faults
Cracked glass, dead display and dead digitizer differ
THE POINT
Diagnose mobile device hardware faults including battery, charging, screen, digitizer, port and overheating problems, applying the correct safety response (Core 1 objective 5.5).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
142

## Slide 143
LAB 26 · VERIFY
Mobile Device Hardware Fault Diagnosis
✅ Expected result
Every fault in your map has both a technical and a safety response; the swollen battery entry forbids puncturing, compressing and charging; and the charging diagnosis substitutes cable and charger before the battery is suspected.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
143

## Slide 144
TOPIC 05 · HANDS-ON
Printer Fault Diagnosis from Print Defects
LAB 27
Diagnose printer faults by reading the physical defect on the page and mapping it to the failed component in the print process (Core 1 objective 5.6).
A printed page is diagnostic evidence: the defect's pattern tells you which component failed and often where in the paper path. You build the defect-to-component map, then work through paper handling, connectivity and driver faults that produce no defect at all.
YOU'LL BUILD
A print defect diagnostic map covering twelve defects, plus a paper-path and connectivity fault checklist.
TOOLCHAIN
Laser and inkjet printers or reference defect images, maintenance kit reference, print management console
DONE WHEN
Your map covers all twelve defects with a named component and a corrective action; the fuser, drum and corona faults are correctly distinguished; and the connectivity checklist includes clearing the queue and restarting the spooler.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
144

## Slide 145
LAB 27 · PROCESS MAP
How Lab 27 Runs
1
Read the page
The defect pattern names the component that failed
2
Trace the drum
Vertical lines and repeating ghost images
3
Trace the fuser
Toner that wipes off was never melted onto the paper
4
Trace paper handling
Jams and misfeeds point at rollers and separation pads
5
Clear the queue
No output at all: spooler, queue, network and driver
THE POINT
Diagnose printer faults by reading the physical defect on the page and mapping it to the failed component in the print process (Core 1 objective 5.6).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
145

## Slide 146
LAB 27 · VERIFY
Printer Fault Diagnosis from Print Defects
✅ Expected result
Your map covers all twelve defects with a named component and a corrective action; the fuser, drum and corona faults are correctly distinguished; and the connectivity checklist includes clearing the queue and restarting the spooler.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
146

## Slide 147
TOPIC 05 · HANDS-ON
Network Fault Diagnosis — Command Line to Packet Level
LAB 28
Diagnose network faults by working the layers in order, from physical connectivity through addressing and DNS to application behaviour (Core 1 objective 5.7).
Network faults are diagnosed layer by layer, because testing at the wrong layer wastes time and misleads. You work a fixed bottom-up sequence with a specific command at each layer, then use packet analysis to resolve what the commands alone cannot.
YOU'LL BUILD
A layered network diagnostic sequence with a command per layer, and a symptom-to-cause map for eight network faults.
TOOLCHAIN
Killercoda Ubuntu Playground, PCAP Analyzer, IP Calculator, ping, traceroute, dig, ss, tcpdump
DONE WHEN
Every command in the sequence runs successfully on the playground, the sequence tests layers strictly bottom-up, IP Calculator confirms the host address sits within its usable range, and the symptom map assigns a layer and a specific test to all eight faults.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
147

## Slide 148
LAB 28 · PROCESS MAP
How Lab 28 Runs
1
Order the layers
Link, addressing, gateway, DNS, then the application
2
Prove the link
ip -brief link show before anything above it
3
Validate the address
APIPA means DHCP never answered; confirm the subnet
4
Split routing from DNS
Ping by IP, then by name, and compare the results
5
Capture when stuck
tcpdump and PCAP Analyzer when commands are inconclusive
THE POINT
Diagnose network faults by working the layers in order, from physical connectivity through addressing and DNS to application behaviour (Core 1 objective 5.7).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
148

## Slide 149
LAB 28 · VERIFY
Network Fault Diagnosis — Command Line to Packet Level
✅ Expected result
Every command in the sequence runs successfully on the playground, the sequence tests layers strictly bottom-up, IP Calculator confirms the host address sits within its usable range, and the symptom map assigns a layer and a specific test to all eight faults.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
149

## Slide 150
TOPIC 05 RECAP · 28% of Core 1
Recap — Hardware and Network Troubleshooting
• You can now: Apply the CompTIA six-step troubleshooting methodology in order to a real fault, documenting each step (Core 1 objective 5.1).
• You can now: Diagnose no-power, no-POST and no-boot faults using beep codes, diagnostic LEDs and a systematic elimination sequence (Core 1 objective 5.2).
• You can now: Diagnose storage faults using S.M.A.R.T. data, symptom analysis and RAID status, and choose the correct recovery action for each RAID level (Core 1 objective 5.3).
• You can now: Diagnose display and projector faults by isolating source, cable, panel, backlight and settings as distinct failure points (Core 1 objective 5.4).
• You can now: Diagnose mobile device hardware faults including battery, charging, screen, digitizer, port and overheating problems, applying the correct safety response (Core 1 objective 5.5).
• You can now: Diagnose printer faults by reading the physical defect on the page and mapping it to the failed component in the print process (Core 1 objective 5.6).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
150

## Slide 151
TOPIC 06
Operating Systems
Windows editions and installation · command line · Windows tools and MMC · file systems · macOS and Linux
06
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
151

## Slide 152
CORE 2 · 28% OF CORE 2
Topic 06 at a Glance — Operating Systems
1
Exam
CompTIA A+ Core 2
2
Domain weighting
28% of Core 2
3
Share of course time
17%
4
Hands-on labs
Lab 29, Lab 30, Lab 31, Lab 32, Lab 33, Lab 34, Lab 35, Lab 36
5
Sub-topics
Windows editions and installation · command line · Windows tools and MMC · file systems · macOS and Linux
6
Why it matters
This domain is assessed in both the WSQ Written Assessment and the Practical Performance.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
152

## Slide 153
TOPIC 06 · 28% of Core 2
Key Concepts — Operating Systems
1
Windows editions differ in capability, and choosing correctly avoids paying for features nobody needs. Home has no domain join or BitLocker, Pro adds domain join, BitLocker, Group Policy and Remote Desktop hosting, and Enterprise adds large-scale management features.
2
Installation types serve different situations: a clean install wipes and starts fresh, an in-place upgrade keeps files and applications, a network deployment images many machines at once over the wire, and cloning duplicates a prepared reference image.
3
MBR partitioning is limited to four primary partitions and 2 TB disks, while GPT supports far more partitions and much larger disks and is required for UEFI Secure Boot. Getting this wrong is a common cause of an installer refusing to proceed.
4
Windows file systems differ in what they can do. NTFS supports permissions, encryption, compression, journaling and very large files. FAT32 is limited to 4 GB files but is universally readable, and exFAT lifts the size limit for removable media.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
153

## Slide 154
TOPIC 06 · 28% of Core 2
Key Concepts — Operating Systems (2)
1
Navigation and file commands you must know are cd, dir, md, rd, copy, xcopy and robocopy — where robocopy is the resilient choice for large or resumable transfers and is what you use in real migrations.
2
Networking commands each answer a specific question: ipconfig /all shows the full configuration, ping tests reachability, tracert shows the path, nslookup queries DNS directly, netstat lists active connections and pathping combines ping and tracert.
3
Repair commands fix specific damage. sfc /scannow repairs protected system files, chkdsk /f fixes file system errors while /r also locates bad sectors, and DISM repairs the component store that sfc itself depends on.
4
Task Manager is the first stop for performance triage — Processes shows what is consuming CPU, memory, disk and network, Performance graphs the trend, and Startup shows what is slowing the boot.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
154

## Slide 155
TOPIC 06 · 28% of Core 2
Key Concepts — Operating Systems (3)
1
The Microsoft Management Console hosts snap-ins you must be able to launch by name: eventvwr.msc, diskmgmt.msc, taskschd.msc, devmgmt.msc, lusrmgr.msc, perfmon.msc and gpedit.msc.
2
Additional utilities cover the rest of the toolkit: msconfig for boot and startup, cleanmgr for disk cleanup, dfrgui to optimise drives, regedit for the registry and resmon for detailed resource analysis.
3
A workgroup is a decentralised peer-to-peer arrangement using local accounts and is right for a SOHO, while a domain centralises authentication and policy in Active Directory and is what any organisation of scale uses.
4
macOS provides Time Machine for backup, Disk Utility for partitioning and First Aid, FileVault for full-disk encryption, Keychain for credentials, Mission Control for window and desktop management, and Gatekeeper to control what may install.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
155

## Slide 156
TOPIC 06 · 28% of Core 2
Key Concepts — Operating Systems (4)
1
Linux command-line essentials are ls, cd, pwd, cp, mv, rm, mkdir, cat, grep, find, df, du, ps, top, chmod, chown, sudo, apt and man. These appear directly in Core 2 objective 1.11.
2
Linux permissions are read, write and execute applied to owner, group and others, expressed either symbolically (rwxr-xr--) or numerically (754). chmod changes the permission bits and chown changes ownership.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
156

## Slide 157
WHAT YOU'LL DO
Hands-On Labs — Operating Systems
Labs 29–31
• Windows Editions, Installation Types and Partitioning
• Windows Command Line — Navigation, Files and Copy Operations
• Windows Networking and Repair Commands
Labs 32–34
• Windows Management Tools — Task Manager, MMC and Snap-ins
• File Systems, Permissions and Share Configuration
• Linux Command Line Essentials on Killercoda
Labs 35–36
• Linux Permissions, Ownership and User Management
• macOS Tools and Cross-Platform File System Compatibility
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
157

## Slide 158
TOPIC 06 · HANDS-ON
Windows Editions, Installation Types and Partitioning
LAB 29
Select the correct Windows edition and installation type for a requirement, and plan MBR or GPT partitioning to match the firmware mode (Core 2 objectives 1.1 and 1.9).
You match Windows editions to requirements, choose the right installation type for each situation, and plan the partition scheme — the decision that determines whether the installer will even proceed, since UEFI Secure Boot requires GPT.
YOU'LL BUILD
An edition selection matrix, four justified installation-type selections and a partition plan matched to the firmware mode.
TOOLCHAIN
Windows installation media or reference, Disk Management, diskpart, msinfo32
DONE WHEN
Your edition matrix correctly identifies which editions support domain join and BitLocker, each installation-type selection is justified against its requirement, and the partition plan matches the firmware mode confirmed in msinfo32.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
158

## Slide 159
LAB 29 · PROCESS MAP
How Lab 29 Runs
1
Match the edition
Home cannot join a domain or run BitLocker
2
Choose the install
Clean, in-place upgrade, network deploy or clone
3
Check the requirements
TPM 2.0, UEFI and Secure Boot for Windows 11
4
Pick the partition style
UEFI Secure Boot needs GPT; legacy BIOS uses MBR
5
Confirm the firmware
msinfo32 states the BIOS mode and Secure Boot state
THE POINT
Select the correct Windows edition and installation type for a requirement, and plan MBR or GPT partitioning to match the firmware mode (Core 2 objectives 1.1 and 1.9).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
159

## Slide 160
LAB 29 · VERIFY
Windows Editions, Installation Types and Partitioning
✅ Expected result
Your edition matrix correctly identifies which editions support domain join and BitLocker, each installation-type selection is justified against its requirement, and the partition plan matches the firmware mode confirmed in msinfo32.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
160

## Slide 161
TOPIC 06 · HANDS-ON
Windows Command Line — Navigation, Files and Copy Operations
LAB 30
Use the Windows command line for navigation, file management and resilient copy operations, choosing correctly between copy, xcopy and robocopy (Core 2 objective 1.2).
You work the Windows command line the way a technician does during a migration or a repair, when the GUI is unavailable or too slow. The lab ends on robocopy, because it is the tool that actually survives a large real-world file migration.
YOU'LL BUILD
A command reference sheet and a completed file migration performed with robocopy, verified against the source.
TOOLCHAIN
Windows PC, Command Prompt, PowerShell
DONE WHEN
Every command executes without error, the robocopy log confirms the expected file count copied, your reference sheet states the specific limitation of copy and xcopy that robocopy overcomes, and the /MIR deletion warning is recorded.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
161

## Slide 162
LAB 30 · PROCESS MAP
How Lab 30 Runs
1
Open an elevated prompt
Confirm where you are and what is available
2
Navigate and list
cd, dir with hidden files, and a recursive listing
3
Copy one file
copy handles files only — no directory trees
4
Copy a tree
xcopy carries subdirectories but cannot resume
5
Mirror with robocopy
Retries, resumes and logs — and /MIR deletes
THE POINT
Use the Windows command line for navigation, file management and resilient copy operations, choosing correctly between copy, xcopy and robocopy (Core 2 objective 1.2).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
162

## Slide 163
LAB 30 · VERIFY
Windows Command Line — Navigation, Files and Copy Operations
✅ Expected result
Every command executes without error, the robocopy log confirms the expected file count copied, your reference sheet states the specific limitation of copy and xcopy that robocopy overcomes, and the /MIR deletion warning is recorded.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
163

## Slide 164
TOPIC 06 · HANDS-ON
Windows Networking and Repair Commands
LAB 31
Use Windows networking and repair commands to diagnose connectivity and repair system file corruption (Core 2 objective 1.2).
You run the diagnostic and repair commands that appear directly in the Core 2 objectives, interpreting the output of each rather than merely executing it — because in support work the output is the diagnosis.
YOU'LL BUILD
A command output interpretation record and a completed system file integrity check with results explained.
TOOLCHAIN
Windows PC, Command Prompt as administrator, PowerShell
DONE WHEN
Every command produces output you have interpreted in writing; ipconfig /all output identifies all six required fields; you correctly state that ping to IP succeeding while ping to name fails means DNS; and the sfc result is recorded with its meaning.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
164

## Slide 165
LAB 31 · PROCESS MAP
How Lab 31 Runs
1
Read the configuration
ipconfig /all gives address, gateway, DNS and MAC
2
Renew the lease
Release and renew to prove the DHCP server answers
3
Test in order
Loopback, gateway, external IP, then external name
4
Isolate DNS
IP works but name fails means DNS and nothing else
5
Repair the system
sfc /scannow, then DISM when sfc cannot repair
THE POINT
Use Windows networking and repair commands to diagnose connectivity and repair system file corruption (Core 2 objective 1.2).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
165

## Slide 166
LAB 31 · VERIFY
Windows Networking and Repair Commands
✅ Expected result
Every command produces output you have interpreted in writing; ipconfig /all output identifies all six required fields; you correctly state that ping to IP succeeding while ping to name fails means DNS; and the sfc result is recorded with its meaning.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
166

## Slide 167
TOPIC 06 · HANDS-ON
Windows Management Tools — Task Manager, MMC and Snap-ins
LAB 32
Use Task Manager, the Microsoft Management Console and its snap-ins to diagnose performance, inspect logs and manage devices, disks, users and tasks (Core 2 objectives 1.3 and 1.4).
You work through every Windows administrative tool named in the Core 2 objectives, launching each by its executable name — because in an exam and on a locked-down machine you need the name, not the Start menu path.
YOU'LL BUILD
A tool reference table with the launch command and primary use for each, plus a performance triage record from Task Manager.
TOOLCHAIN
Windows PC, Task Manager, MMC snap-ins, Control Panel, Windows Settings
DONE WHEN
Your table lists at least twelve tools with the correct launch command for each; the Task Manager triage names the top CPU, memory and disk consumer; and the Event Viewer record cites at least one real error with its source and event ID.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
167

## Slide 168
LAB 32 · PROCESS MAP
How Lab 32 Runs
1
Triage in Task Manager
Sort by CPU, then memory, then disk
2
Trim the startup
Disable the high-impact items that slow the boot
3
Read the logs
Event Viewer, filtered to errors in the last 24 hours
4
Open the snap-ins
diskmgmt, devmgmt, taskschd, lusrmgr and perfmon
5
Complete the toolkit
msconfig, cleanmgr, dfrgui, regedit and resmon
THE POINT
Use Task Manager, the Microsoft Management Console and its snap-ins to diagnose performance, inspect logs and manage devices, disks, users and tasks (Core 2 objectives 1.3 and 1.4).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
168

## Slide 169
LAB 32 · VERIFY
Windows Management Tools — Task Manager, MMC and Snap-ins
✅ Expected result
Your table lists at least twelve tools with the correct launch command for each; the Task Manager triage names the top CPU, memory and disk consumer; and the Event Viewer record cites at least one real error with its source and event ID.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
169

## Slide 170
TOPIC 06 · HANDS-ON
File Systems, Permissions and Share Configuration
LAB 33
Compare NTFS, FAT32 and exFAT, and configure NTFS and share permissions correctly, applying the most-restrictive rule (Core 2 objectives 1.9 and 2.5).
You compare the Windows file systems on the limits that decide which to use, then configure both NTFS and share permissions on the same folder and prove the most-restrictive rule — the single most misunderstood permission behaviour in Windows.
YOU'LL BUILD
A file system comparison table and a configured share demonstrating the effective permission when NTFS and share permissions differ.
TOOLCHAIN
Windows PC, File Explorer, icacls, net share, Disk Management
DONE WHEN
Your comparison table states the 4 GB FAT32 file size limit and identifies which file systems support permissions; icacls confirms the granted permission; and you correctly state that Share Full Control combined with NTFS Read yields an effective permission of Read.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
170

## Slide 171
LAB 33 · PROCESS MAP
How Lab 33 Runs
1
Compare file systems
NTFS, FAT32 and exFAT on size, permissions and reach
2
Recall the hard limit
FAT32 cannot hold a file larger than 4 GB
3
Read the ACL
icacls shows granted rights and what is inherited
4
Grant and share
Set an NTFS right, then share with a different one
5
Apply most-restrictive
Share Full Control with NTFS Read yields Read
THE POINT
Compare NTFS, FAT32 and exFAT, and configure NTFS and share permissions correctly, applying the most-restrictive rule (Core 2 objectives 1.9 and 2.5).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
171

## Slide 172
LAB 33 · VERIFY
File Systems, Permissions and Share Configuration
✅ Expected result
Your comparison table states the 4 GB FAT32 file size limit and identifies which file systems support permissions; icacls confirms the granted permission; and you correctly state that Share Full Control combined with NTFS Read yields an effective permission of Read.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
172

## Slide 173
TOPIC 06 · HANDS-ON
Linux Command Line Essentials on Killercoda
LAB 34
Use the Linux commands named in Core 2 objective 1.11 for navigation, file management, searching, process control and package management (Core 2 objective 1.11).
You work every Linux command the A+ objectives name, on a real Ubuntu machine in the browser. Each command is run against real files and real output so the behaviour, not just the syntax, is what you take away.
YOU'LL BUILD
A verified Linux command reference with real output recorded for each command in the objective list.
TOOLCHAIN
Killercoda Ubuntu Playground (https://killercoda.com/playgrounds/scenario/ubuntu)
DONE WHEN
Every command runs without error on the playground; grep returns exactly two ERROR lines from the log; ls -l confirms the 640 permission as rw-r-----; and your reference records real output for each command rather than expected output.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
173

## Slide 174
LAB 34 · PROCESS MAP
How Lab 34 Runs
1
Open the playground
Confirm the working directory and the current user
2
Build a tree
Directories and files with real content to work on
3
List and read
ls -la, cat and less on real system files
4
Search the content
grep finds the errors; find locates the files
5
Check and control
df, free, ps, then chmod and chown
THE POINT
Use the Linux commands named in Core 2 objective 1.11 for navigation, file management, searching, process control and package management (Core 2 objective 1.11).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
174

## Slide 175
LAB 34 · VERIFY
Linux Command Line Essentials on Killercoda
✅ Expected result
Every command runs without error on the playground; grep returns exactly two ERROR lines from the log; ls -l confirms the 640 permission as rw-r-----; and your reference records real output for each command rather than expected output.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
175

## Slide 176
TOPIC 06 · HANDS-ON
Linux Permissions, Ownership and User Management
LAB 35
Apply the Linux permission model to users, groups and others using symbolic and numeric notation, and manage users and sudo rights (Core 2 objective 1.11).
You work the permission model until numeric notation is automatic, then apply it to a real access-control problem: giving a group shared write access to a directory without giving everyone else access. This is exactly what the exam tests and what the job requires.
YOU'LL BUILD
A permission notation conversion table and a working shared group directory with verified access control.
TOOLCHAIN
Killercoda Ubuntu Playground
DONE WHEN
Your conversion table is correct for all seven modes; the execute-bit demonstration shows a directory becoming enterable at 755 but not at 644; /srv/shared is mode 2770 owned by the support group; and alice's file inherits the support group.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
176

## Slide 177
LAB 35 · PROCESS MAP
How Lab 35 Runs
1
Read the triplets
Owner, group and others, each with r, w and x
2
Convert the notation
r is 4, w is 2, x is 1, so rw- is 6 and rwx is 7
3
Prove the execute bit
A directory at 644 cannot be entered at all
4
Create users and a group
Two accounts sharing one support group
5
Share with setgid
Mode 2770 so new files inherit the group
THE POINT
Apply the Linux permission model to users, groups and others using symbolic and numeric notation, and manage users and sudo rights (Core 2 objective 1.11).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
177

## Slide 178
LAB 35 · VERIFY
Linux Permissions, Ownership and User Management
✅ Expected result
Your conversion table is correct for all seven modes; the execute-bit demonstration shows a directory becoming enterable at 755 but not at 644; /srv/shared is mode 2770 owned by the support group; and alice's file inherits the support group.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
178

## Slide 179
TOPIC 06 · HANDS-ON
macOS Tools and Cross-Platform File System Compatibility
LAB 36
Identify macOS features and utilities and resolve cross-platform file system compatibility between Windows, macOS and Linux (Core 2 objectives 1.10 and 1.9).
You map the macOS toolset to its Windows equivalent, which is how a technician supporting a mixed fleet actually thinks, then solve the file system compatibility problem that causes most cross-platform support tickets.
YOU'LL BUILD
A macOS-to-Windows tool equivalence table and a solved cross-platform file system compatibility matrix.
TOOLCHAIN
macOS device or reference material, Windows PC, file system documentation
DONE WHEN
Your equivalence table maps at least eight macOS tools to their Windows counterparts; the compatibility matrix correctly shows macOS as read-only for NTFS; and both scenarios name a file system and justify it against the stated constraints.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
179

## Slide 180
LAB 36 · PROCESS MAP
How Lab 36 Runs
1
Map the equivalents
Time Machine, Disk Utility, FileVault and Keychain
2
Explain Gatekeeper
It decides which applications are allowed to run
3
Rank the sources
App Store, signed installer, then unsigned
4
Table the file systems
Read and write support across the three platforms
5
Solve the exchange
macOS reads NTFS but cannot write to it
THE POINT
Identify macOS features and utilities and resolve cross-platform file system compatibility between Windows, macOS and Linux (Core 2 objectives 1.10 and 1.9).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
180

## Slide 181
LAB 36 · VERIFY
macOS Tools and Cross-Platform File System Compatibility
✅ Expected result
Your equivalence table maps at least eight macOS tools to their Windows counterparts; the compatibility matrix correctly shows macOS as read-only for NTFS; and both scenarios name a file system and justify it against the stated constraints.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
181

## Slide 182
TOPIC 06 RECAP · 28% of Core 2
Recap — Operating Systems
• You can now: Select the correct Windows edition and installation type for a requirement, and plan MBR or GPT partitioning to match the firmware mode (Core 2 objectives 1.1 and 1.9).
• You can now: Use the Windows command line for navigation, file management and resilient copy operations, choosing correctly between copy, xcopy and robocopy (Core 2 objective 1.2).
• You can now: Use Windows networking and repair commands to diagnose connectivity and repair system file corruption (Core 2 objective 1.2).
• You can now: Use Task Manager, the Microsoft Management Console and its snap-ins to diagnose performance, inspect logs and manage devices, disks, users and tasks (Core 2 objectives 1.3 and 1.4).
• You can now: Compare NTFS, FAT32 and exFAT, and configure NTFS and share permissions correctly, applying the most-restrictive rule (Core 2 objectives 1.9 and 2.5).
• You can now: Use the Linux commands named in Core 2 objective 1.11 for navigation, file management, searching, process control and package management (Core 2 objective 1.11).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
182

## Slide 183
TOPIC 07
Security
Physical and logical security · authentication and MFA · wireless security · malware · social engineering · workstation and mobile hardening
07
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
183

## Slide 184
CORE 2 · 28% OF CORE 2
Topic 07 at a Glance — Security
1
Exam
CompTIA A+ Core 2
2
Domain weighting
28% of Core 2
3
Share of course time
17%
4
Hands-on labs
Lab 37, Lab 38, Lab 39, Lab 40, Lab 41, Lab 42, Lab 43, Lab 44
5
Sub-topics
Physical and logical security · authentication and MFA · wireless security · malware · social engineering · workstation and mobile hardening
6
Why it matters
This domain is assessed in both the WSQ Written Assessment and the Practical Performance.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
184

## Slide 185
TOPIC 07 · 28% of Core 2
Key Concepts — Security
1
Physical controls stop an attacker reaching the hardware at all: access control vestibules defeat tailgating, badge readers and biometrics control entry, cameras and alarms detect intrusion, and bollards and fences protect the perimeter.
2
The principle of least privilege gives every user exactly the access their job requires and nothing more, which limits the blast radius when any single account is compromised.
3
Multifactor authentication combines factors from different categories — something you know, something you have and something you are. Two passwords are not MFA because both come from the same category.
4
Wireless security has a clear generational order. WEP is broken, WPA with TKIP is deprecated, WPA2 with AES-CCMP is the practical minimum today, and WPA3 adds SAE which defeats offline dictionary attacks against the handshake.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
185

## Slide 186
TOPIC 07 · 28% of Core 2
Key Concepts — Security (2)
1
Enterprise authentication is centralised through RADIUS, TACACS+ or Kerberos so that credentials live in one directory rather than being configured device by device.
2
Malware types are distinguished by behaviour: a virus needs a host file and human action, a worm spreads by itself across a network, a trojan hides inside apparently legitimate software, ransomware encrypts data for payment, a rootkit hides at or below the OS, spyware exfiltrates information, and a keylogger records what you type.
3
The seven-step malware removal procedure is examinable in order: investigate and verify symptoms, quarantine the system, disable System Restore, remediate by updating the anti-malware and scanning in safe mode, schedule scans and updates, re-enable System Restore and create a restore point, and finally educate the end user.
4
Social engineering attacks the person, not the machine. Phishing, spear phishing, whaling, vishing and smishing all use a fabricated pretext and manufactured urgency to get the target to act before they think.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
186

## Slide 187
TOPIC 07 · 28% of Core 2
Key Concepts — Security (3)
1
In-person techniques include tailgating through a controlled door, shoulder surfing to read credentials, dumpster diving for discarded information, and impersonating IT support or a senior executive.
2
Network attacks you must recognise are denial of service and its distributed form, on-path (man-in-the-middle) interception, DNS poisoning, ARP spoofing, SQL injection, cross-site scripting and the zero-day exploit for which no patch yet exists.
3
Windows security settings that matter in practice are Defender Antivirus with current definitions, Defender Firewall, NTFS and share permissions where the most restrictive of the two wins, User Account Control, and BitLocker for full-volume encryption.
4
Workstation hardening means strong password policies, account lockout thresholds, screensaver locks, disabling AutoRun, removing unused accounts and restricting administrative rights to those who genuinely need them.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
187

## Slide 188
TOPIC 07 · 28% of Core 2
Key Concepts — Security (4)
1
Mobile hardening relies on screen locks, biometrics, full-device encryption, remote wipe, locator services, current OS patches and installing applications only from the official store.
2
Data destruction must match the sensitivity of the data. Physical destruction by drilling, shredding, degaussing or incinerating is irreversible, while wiping and low-level formatting allow reuse — and outsourced destruction must return a certificate.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
188

## Slide 189
WHAT YOU'LL DO
Hands-On Labs — Security
Labs 37–39
• Physical and Logical Security Control Design
• Password Strength Analysis and Authentication Policy
• Phishing Recognition and Social Engineering Defence
Labs 40–42
• Malware Types, Symptoms and the Seven-Step Removal Procedure
• Network Attack Recognition — Injection, XSS and Data Leakage
• Wireless Security and SOHO Router Hardening
Labs 43–44
• Windows Security Configuration and BitLocker Encryption
• Data Destruction, Disposal and Regulated Data Handling
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
189

## Slide 190
TOPIC 07 · HANDS-ON
Physical and Logical Security Control Design
LAB 37
Select and justify physical and logical security controls for a site, applying the principle of least privilege and defence in depth (Core 2 objectives 2.1 and 2.2).
You design the control set for a small office, working outward from the data to the perimeter. Each control must be justified by the specific threat it defeats, because a control chosen without a threat is a cost without a benefit.
YOU'LL BUILD
A layered security design with physical and logical controls, each mapped to the threat it defeats.
TOOLCHAIN
Site plan or scenario brief, security control reference, organisational policy template
DONE WHEN
Every control in your design is mapped to a specific threat; tailgating and piggybacking are correctly distinguished; the MFA section correctly rejects two same-category factors; and your first-three prioritisation is justified on risk rather than cost alone.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
190

## Slide 191
LAB 37 · PROCESS MAP
How Lab 37 Runs
1
Layer the defences
Defeating one control still leaves another
2
Secure the perimeter
Fences, bollards, lighting, cameras and alarms
3
Control the entry
A vestibule admits one person and defeats tailgating
4
Apply least privilege
Exactly the access the role requires, and no more
5
Require real MFA
Two factors from different categories, never two passwords
THE POINT
Select and justify physical and logical security controls for a site, applying the principle of least privilege and defence in depth (Core 2 objectives 2.1 and 2.2).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
191

## Slide 192
LAB 37 · VERIFY
Physical and Logical Security Control Design
✅ Expected result
Every control in your design is mapped to a specific threat; tailgating and piggybacking are correctly distinguished; the MFA section correctly rejects two same-category factors; and your first-three prioritisation is justified on risk rather than cost alone.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
192

## Slide 193
TOPIC 07 · HANDS-ON
Password Strength Analysis and Authentication Policy
LAB 38
Analyse password strength quantitatively and write an authentication policy grounded in entropy and crack-time evidence (Core 2 objectives 2.2 and 2.6).
You use the Cybersecurity Simulator's Password Lab to measure real passwords rather than assert what makes a good one, then write a policy whose every rule is justified by the measured effect on entropy and crack time.
YOU'LL BUILD
A measured password analysis table and an authentication policy with each rule justified by evidence.
TOOLCHAIN
Cybersecurity Simulator Password Lab (https://alfredang.github.io/cybersecuritysimulator/), policy template
DONE WHEN
Your analysis table records the actual entropy and crack time from the tool for all five passwords; the conclusion that length beats substitution is supported by your own figures; and every policy rule cites a measured value.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
193

## Slide 194
LAB 38 · PROCESS MAP
How Lab 38 Runs
1
Open the Password Lab
Measure rather than assert what makes a password strong
2
Test a dictionary word
Record strength, crack time and entropy in bits
3
Test the substitution
P@ssw0rd is what cracking tools try first
4
Test a passphrase
Compare a 16-character phrase against the substitution
5
Write the policy
Every rule justified by a measured figure
THE POINT
Analyse password strength quantitatively and write an authentication policy grounded in entropy and crack-time evidence (Core 2 objectives 2.2 and 2.6).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
194

## Slide 195
LAB 38 · VERIFY
Password Strength Analysis and Authentication Policy
✅ Expected result
Your analysis table records the actual entropy and crack time from the tool for all five passwords; the conclusion that length beats substitution is supported by your own figures; and every policy rule cites a measured value.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
195

## Slide 196
TOPIC 07 · HANDS-ON
Phishing Recognition and Social Engineering Defence
LAB 39
Identify phishing indicators and social engineering tactics, and design the user awareness training that defends against them (Core 2 objectives 2.4 and 2.7).
You work the Cybersecurity Simulator's phishing and social engineering modules to build recognition from real examples, then convert what you learned into the awareness training an organisation would actually deliver.
YOU'LL BUILD
A phishing indicator checklist, a social engineering tactic reference and a user awareness training outline.
TOOLCHAIN
Cybersecurity Simulator (https://alfredang.github.io/cybersecuritysimulator/) — Phishing and Social Engineering modules
DONE WHEN
Your checklist covers at least seven phishing indicators; the tactic reference defines and defends all eight social engineering tactics; the phishing variants are correctly distinguished by target and channel; and the training outline includes a reporting procedure.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
196

## Slide 197
LAB 39 · PROCESS MAP
How Lab 39 Runs
1
Classify the mail
Ten emails across six categories, safe or phishing
2
Review your misses
Record the indicator you missed on each one
3
Inspect the link
The URL inspector reveals the real destination
4
Work the tactics
Pretexting, baiting, tailgating, vishing and smishing
5
Design the training
Objectives, scenarios, a retention test and reporting
THE POINT
Identify phishing indicators and social engineering tactics, and design the user awareness training that defends against them (Core 2 objectives 2.4 and 2.7).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
197

## Slide 198
LAB 39 · VERIFY
Phishing Recognition and Social Engineering Defence
✅ Expected result
Your checklist covers at least seven phishing indicators; the tactic reference defines and defends all eight social engineering tactics; the phishing variants are correctly distinguished by target and channel; and the training outline includes a reporting procedure.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
198

## Slide 199
TOPIC 07 · HANDS-ON
Malware Types, Symptoms and the Seven-Step Removal Procedure
LAB 40
Identify malware types by behaviour and apply the CompTIA seven-step malware removal procedure in order (Core 2 objectives 2.3 and 3.3).
You study malware behaviour safely in the simulator, then learn the seven-step removal procedure in order — because the order is examinable and, more importantly, because doing step four before step three re-infects the restore points you are relying on.
YOU'LL BUILD
A malware type reference and a written seven-step removal procedure applied to a specific infection scenario.
TOOLCHAIN
Cybersecurity Simulator (https://alfredang.github.io/cybersecuritysimulator/) — Malware, Virus and Ransomware modules
DONE WHEN
Your reference table covers at least eight malware types with propagation and symptoms; the seven steps are in the correct order; you correctly explain why System Restore is disabled before remediation; and the scenario has a specific action at every step.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
199

## Slide 200
LAB 40 · PROCESS MAP
How Lab 40 Runs
1
Watch it spread
One infected host on a flat network is an org problem
2
See the ransom screen
Do not pay; isolate, identify, then restore offline
3
Table the malware
Virus, worm, trojan, rootkit, spyware and keylogger
4
Learn the seven steps
Verify, quarantine, disable restore, remediate, then educate
5
Explain the order
Restore points can carry the malware straight back
THE POINT
Identify malware types by behaviour and apply the CompTIA seven-step malware removal procedure in order (Core 2 objectives 2.3 and 3.3).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
200

## Slide 201
LAB 40 · VERIFY
Malware Types, Symptoms and the Seven-Step Removal Procedure
✅ Expected result
Your reference table covers at least eight malware types with propagation and symptoms; the seven steps are in the correct order; you correctly explain why System Restore is disabled before remediation; and the scenario has a specific action at every step.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
201

## Slide 202
TOPIC 07 · HANDS-ON
Network Attack Recognition — Injection, XSS and Data Leakage
LAB 41
Recognise common application and network attacks including SQL injection, cross-site scripting, on-path attacks and denial of service, and state the defence for each (Core 2 objective 2.4).
You see injection and scripting attacks behave in the simulator's safe sandbox, then build the attack reference an A+ technician needs — not to perform these attacks, but to recognise their symptoms in a ticket and escalate correctly.
YOU'LL BUILD
An attack reference table with mechanism, symptom and defence for each attack, plus a data leakage risk assessment.
TOOLCHAIN
Cybersecurity Simulator (https://alfredang.github.io/cybersecuritysimulator/) — SQL Injection, XSS and Data Leakage modules
DONE WHEN
Your table covers at least eight attacks with mechanism, symptom and defence; you correctly explain why ' OR '1'='1 bypasses authentication; the data leakage assessment names the highest-impact practice from the measured score; and the escalation boundary is stated.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
202

## Slide 203
LAB 41 · PROCESS MAP
How Lab 41 Runs
1
Break the query
' OR '1'='1 makes the condition always true
2
Defend the input
Parameterised queries so input cannot alter structure
3
Compare the rendering
Safe output encoding against unsafe injection
4
Score the leakage
Toggle six practices and watch the risk move
5
Know your boundary
Recognise, isolate, preserve evidence, then escalate
THE POINT
Recognise common application and network attacks including SQL injection, cross-site scripting, on-path attacks and denial of service, and state the defence for each (Core 2 objective 2.4).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
203

## Slide 204
LAB 41 · VERIFY
Network Attack Recognition — Injection, XSS and Data Leakage
✅ Expected result
Your table covers at least eight attacks with mechanism, symptom and defence; you correctly explain why ' OR '1'='1 bypasses authentication; the data leakage assessment names the highest-impact practice from the measured score; and the escalation boundary is stated.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
204

## Slide 205
TOPIC 07 · HANDS-ON
Wireless Security and SOHO Router Hardening
LAB 42
Configure wireless encryption and harden a SOHO router against the attacks the default configuration invites (Core 2 objectives 2.9 and 2.10).
A SOHO router shipped with default settings is one of the most commonly compromised devices in any small network. You work through every hardening step in order of impact and record what each one actually defeats.
YOU'LL BUILD
A completed router hardening checklist with the threat each step defeats, and a wireless security configuration record.
TOOLCHAIN
SOHO router or emulator, Wi-Fi analyser, IP Calculator, router documentation
DONE WHEN
Your checklist covers at least ten hardening steps each with a named threat; WEP, WPA, WPA2 and WPA3 are correctly ordered by security; SSID hiding and MAC filtering are correctly described as weak controls; and firmware update appears in your five-minute priority set.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
205

## Slide 206
LAB 42 · PROCESS MAP
How Lab 42 Runs
1
Order the encryption
WEP broken, WPA deprecated, WPA2 minimum, WPA3 current
2
Change the defaults
Admin password and SSID before anything else
3
Set WPA2 or WPA3
AES-CCMP with a passphrase of at least 16 characters
4
Know the weak controls
Hidden SSID and MAC filtering stop nobody capable
5
Patch and reduce
Firmware first, then disable WPS, remote admin and UPnP
THE POINT
Configure wireless encryption and harden a SOHO router against the attacks the default configuration invites (Core 2 objectives 2.9 and 2.10).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
206

## Slide 207
LAB 42 · VERIFY
Wireless Security and SOHO Router Hardening
✅ Expected result
Your checklist covers at least ten hardening steps each with a named threat; WEP, WPA, WPA2 and WPA3 are correctly ordered by security; SSID hiding and MAC filtering are correctly described as weak controls; and firmware update appears in your five-minute priority set.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
207

## Slide 208
TOPIC 07 · HANDS-ON
Windows Security Configuration and BitLocker Encryption
LAB 43
Configure Windows security settings including Defender, the firewall, UAC, account policy and BitLocker encryption (Core 2 objectives 2.5 and 2.6).
You configure and verify every Windows security setting the Core 2 objectives name, on a real machine, recording the command that checks each one — because in support work you need to verify state quickly, not click through settings pages.
YOU'LL BUILD
A verified Windows security configuration record with a check command for each setting.
TOOLCHAIN
Windows PC, Windows Security, Defender Firewall, gpedit, BitLocker, PowerShell as administrator
DONE WHEN
Every check command returns output you have recorded; Defender is confirmed enabled with a definition date; all three firewall profiles have a recorded state; net accounts output is captured; and the BitLocker record states where the recovery key is stored.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
208

## Slide 209
LAB 43 · PROCESS MAP
How Lab 43 Runs
1
Check the defences
Defender, firewall, app control and device security
2
Confirm the definitions
Signatures cannot catch what they do not yet know
3
Read all three profiles
Domain, private and public firewall state
4
Inspect UAC and accounts
Prompt level, local users and who holds admin
5
Verify BitLocker
Protection state, method, and where the key is stored
THE POINT
Configure Windows security settings including Defender, the firewall, UAC, account policy and BitLocker encryption (Core 2 objectives 2.5 and 2.6).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
209

## Slide 210
LAB 43 · VERIFY
Windows Security Configuration and BitLocker Encryption
✅ Expected result
Every check command returns output you have recorded; Defender is confirmed enabled with a definition date; all three firewall profiles have a recorded state; net accounts output is captured; and the BitLocker record states where the recovery key is stored.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
210

## Slide 211
TOPIC 07 · HANDS-ON
Data Destruction, Disposal and Regulated Data Handling
LAB 44
Select the correct data destruction method for a stated sensitivity and retention requirement, and handle regulated data according to its legal obligations (Core 2 objectives 2.8 and 4.6).
Data destruction is where a wrong choice creates legal liability rather than an inconvenience. You match destruction methods to data sensitivity, then work the regulated data categories and the chain-of-custody discipline that evidence handling requires.
YOU'LL BUILD
A destruction method decision table, a regulated data handling reference and a completed chain-of-custody form.
TOOLCHAIN
Data destruction reference, regulatory documentation, chain-of-custody template
DONE WHEN
Your decision table gives a method for all four sensitivity levels; you correctly state that degaussing does not work on SSDs; the regulated data reference covers at least five frameworks with obligations; and the chain-of-custody form has no gaps between handovers.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
211

## Slide 212
LAB 44 · PROCESS MAP
How Lab 44 Runs
1
Split the goal
Destroy the media, or sanitise it for reuse
2
Choose destruction
Drill, shred, degauss or incinerate — and get a certificate
3
Know the SSD exception
Degaussing does nothing to flash storage
4
Sanitise correctly
A format only clears the index; overwrite or crypto-erase
5
Handle regulated data
PII, PCI DSS, GDPR, HIPAA and PDPA, with a custody chain
THE POINT
Select the correct data destruction method for a stated sensitivity and retention requirement, and handle regulated data according to its legal obligations (Core 2 objectives 2.8 and 4.6).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
212

## Slide 213
LAB 44 · VERIFY
Data Destruction, Disposal and Regulated Data Handling
✅ Expected result
Your decision table gives a method for all four sensitivity levels; you correctly state that degaussing does not work on SSDs; the regulated data reference covers at least five frameworks with obligations; and the chain-of-custody form has no gaps between handovers.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
213

## Slide 214
TOPIC 07 RECAP · 28% of Core 2
Recap — Security
• You can now: Select and justify physical and logical security controls for a site, applying the principle of least privilege and defence in depth (Core 2 objectives 2.1 and 2.2).
• You can now: Analyse password strength quantitatively and write an authentication policy grounded in entropy and crack-time evidence (Core 2 objectives 2.2 and 2.6).
• You can now: Identify phishing indicators and social engineering tactics, and design the user awareness training that defends against them (Core 2 objectives 2.4 and 2.7).
• You can now: Identify malware types by behaviour and apply the CompTIA seven-step malware removal procedure in order (Core 2 objectives 2.3 and 3.3).
• You can now: Recognise common application and network attacks including SQL injection, cross-site scripting, on-path attacks and denial of service, and state the defence for each (Core 2 objective 2.4).
• You can now: Configure wireless encryption and harden a SOHO router against the attacks the default configuration invites (Core 2 objectives 2.9 and 2.10).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
214

## Slide 215
TOPIC 08
Software Troubleshooting
Windows OS symptoms · recovery tools · malware removal · browser problems · mobile OS and application faults
08
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
215

## Slide 216
CORE 2 · 23% OF CORE 2
Topic 08 at a Glance — Software Troubleshooting
1
Exam
CompTIA A+ Core 2
2
Domain weighting
23% of Core 2
3
Share of course time
8%
4
Hands-on labs
Lab 45, Lab 46, Lab 47, Lab 48, Lab 49
5
Sub-topics
Windows OS symptoms · recovery tools · malware removal · browser problems · mobile OS and application faults
6
Why it matters
This domain is assessed in both the WSQ Written Assessment and the Practical Performance.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
216

## Slide 217
TOPIC 08 · 23% of Core 2
Key Concepts — Software Troubleshooting
1
The common repair sequence escalates from cheap to expensive: reboot, restart the service, uninstall or reinstall the application, add resources, verify requirements, run the system file checker, use System Restore, repair Windows, then reimage as the last resort.
2
Windows recovery options differ in what they preserve. System Restore rolls back system files and the registry but not personal data, Reset reinstalls Windows with an option to keep files, and the Windows Recovery Environment provides startup repair and a command prompt when Windows will not boot.
3
A blue screen of death is caused by a driver fault, failing RAM or disk corruption. Record the stop code, roll back the most recent driver or update, and run memory and disk diagnostics before replacing hardware.
4
Sluggish performance is diagnosed with Task Manager and Resource Monitor to find which resource is saturated — CPU, memory, disk or network — and only then treated by trimming startup items, adding RAM or replacing a failing disk.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
217

## Slide 218
TOPIC 08 · 23% of Core 2
Key Concepts — Software Troubleshooting (2)
1
A 'no OS found' message means the firmware cannot find a boot loader: check the boot order, remove any USB device that is being booted first, confirm the disk is detected, and repair the boot record from the recovery environment.
2
Malware symptoms include unexpected pop-ups, browser redirection, certificate warnings, sudden slowdown, disabled security tools and unexplained network traffic — and any of them justifies quarantining the machine immediately.
3
Browser problems map to specific causes: certificate warnings mean an expired, untrusted or misconfigured certificate, redirection points at adware or a hijacked search provider, and rogue extensions must be removed from the browser rather than from Windows.
4
Mobile application faults are treated in a fixed order — force close, clear the cache, clear the application data, uninstall and reinstall, then check for OS and application updates.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
218

## Slide 219
TOPIC 08 · 23% of Core 2
Key Concepts — Software Troubleshooting (3)
1
Mobile performance symptoms have common causes: battery drain from background applications or a weak signal forcing the radio to full power, overheating from sustained load or charging faults, and random reboots from a failing update or a swollen battery.
2
Mobile security symptoms — high data usage, unexpected ads, sluggish response and unfamiliar applications — often trace back to sideloaded APKs, a rooted or jailbroken device, or an application spoofing a legitimate one.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
219

## Slide 220
WHAT YOU'LL DO
Hands-On Labs — Software Troubleshooting
Labs 45–46
• Windows OS Symptom Diagnosis and Recovery Tools
• Log Analysis with Regular Expressions
Labs 47–48
• Malware Symptom Response and Browser Problem Resolution
• Mobile OS and Application Troubleshooting
Lab 49
• System Restore, Backup Verification and Recovery Testing
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
220

## Slide 221
TOPIC 08 · HANDS-ON
Windows OS Symptom Diagnosis and Recovery Tools
LAB 45
Diagnose common Windows symptoms and select the correct recovery tool, escalating from least to most destructive (Core 2 objectives 3.1 and 3.2).
Windows recovery tools differ in what they destroy, so choosing correctly is what separates a fixed machine from a rebuilt one. You build the escalation ladder, then map each Windows symptom to the lowest rung that will actually resolve it.
YOU'LL BUILD
A recovery tool escalation ladder and a symptom-to-tool map covering ten Windows symptoms.
TOOLCHAIN
Windows PC, System Restore, Windows Recovery Environment, Event Viewer, msconfig, sfc, DISM
DONE WHEN
Your ladder orders all ten recovery options from least to most destructive; the symptom map assigns each of ten symptoms to a specific rung with justification; and you correctly state that System Restore does not affect personal files.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
221

## Slide 222
LAB 45 · PROCESS MAP
How Lab 45 Runs
1
Build the ladder
Reboot first, reimage last, and everything between
2
Start at the bottom
Every rung up costs the user more time and more risk
3
Know what restore does
System files and registry, never personal data
4
Find the saturation
Task Manager and Resource Monitor before treating anything
5
Reach recovery
Three failed boots, or Shift while selecting Restart
THE POINT
Diagnose common Windows symptoms and select the correct recovery tool, escalating from least to most destructive (Core 2 objectives 3.1 and 3.2).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
222

## Slide 223
LAB 45 · VERIFY
Windows OS Symptom Diagnosis and Recovery Tools
✅ Expected result
Your ladder orders all ten recovery options from least to most destructive; the symptom map assigns each of ten symptoms to a specific rung with justification; and you correctly state that System Restore does not affect personal files.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
223

## Slide 224
TOPIC 08 · HANDS-ON
Log Analysis with Regular Expressions
LAB 46
Filter and parse system logs with regular expressions to isolate the events that matter during troubleshooting (Core 2 objectives 3.1 and 4.8).
Logs contain thousands of lines and perhaps three that matter. You build the regular expressions that find those three, testing each pattern in RegexLab before applying it to real log data on the Killercoda playground.
YOU'LL BUILD
A tested regular expression library for log analysis, applied to real log files with the matches verified.
TOOLCHAIN
RegexLab (https://alfredang.github.io/regexgenerator/), Killercoda Ubuntu Playground, grep
DONE WHEN
Every pattern is verified in RegexLab with its match count recorded; the severity grep returns exactly four lines from the log; the IP extraction returns four unique addresses; and the combined query correctly returns only the addresses from error and critical lines.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
224

## Slide 225
LAB 46 · PROCESS MAP
How Lab 46 Runs
1
Learn the building blocks
Digit, word, space classes plus anchors and groups
2
Match an address
Test the IPv4 pattern and record the match count
3
Match the severity
Alternation with the ignore-case flag
4
Understand the flags
g for all matches, i for case, m for multiline
5
Apply it to a log
grep with the proven pattern against real data
THE POINT
Filter and parse system logs with regular expressions to isolate the events that matter during troubleshooting (Core 2 objectives 3.1 and 4.8).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
225

## Slide 226
LAB 46 · VERIFY
Log Analysis with Regular Expressions
✅ Expected result
Every pattern is verified in RegexLab with its match count recorded; the severity grep returns exactly four lines from the log; the IP extraction returns four unique addresses; and the combined query correctly returns only the addresses from error and critical lines.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
226

## Slide 227
TOPIC 08 · HANDS-ON
Malware Symptom Response and Browser Problem Resolution
LAB 47
Recognise malware and browser symptoms, apply the containment sequence and resolve browser-specific problems (Core 2 objectives 3.2 and 3.3).
Browser symptoms are how most malware infections are first reported, and the containment sequence matters more than the cleanup: a machine left on the network while you investigate keeps spreading. You build both the symptom map and the response sequence.
YOU'LL BUILD
A malware and browser symptom map with the response sequence and the containment decision point for each.
TOOLCHAIN
Cybersecurity Simulator, Windows PC, browser settings, Windows Security
DONE WHEN
Your map covers at least eight malware symptoms and four browser symptoms with a response for each; network disconnection appears as the first containment action; the certificate warning causes are correctly separated; and post-cleanup verification includes checking persistence mechanisms.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
227

## Slide 228
LAB 47 · PROCESS MAP
How Lab 47 Runs
1
Contain it first
Disconnect from the network before investigating
2
List the symptoms
Pop-ups, redirection, slowdown and disabled tools
3
Read the certificate
Expired, self-signed, wrong clock or interception
4
Clean the browser
Search provider, extensions, proxy and shortcut target
5
Verify and educate
Recheck persistence, then explain how it arrived
THE POINT
Recognise malware and browser symptoms, apply the containment sequence and resolve browser-specific problems (Core 2 objectives 3.2 and 3.3).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
228

## Slide 229
LAB 47 · VERIFY
Malware Symptom Response and Browser Problem Resolution
✅ Expected result
Your map covers at least eight malware symptoms and four browser symptoms with a response for each; network disconnection appears as the first containment action; the certificate warning causes are correctly separated; and post-cleanup verification includes checking persistence mechanisms.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
229

## Slide 230
TOPIC 08 · HANDS-ON
Mobile OS and Application Troubleshooting
LAB 48
Diagnose and resolve mobile operating system and application faults including crashes, connectivity, battery and performance problems (Core 2 objectives 3.4 and 3.5).
Mobile faults have a fixed escalation order that resolves the large majority without data loss. You work that order on a real device, then handle the security-related symptoms that indicate something worse than a misbehaving app.
YOU'LL BUILD
A mobile troubleshooting escalation sequence and a security symptom map with the response for each.
TOOLCHAIN
Android or iOS device, application settings, device settings, mobile OS documentation
DONE WHEN
Your sequence orders the five application steps from least to most destructive; the cache-versus-data distinction is stated with its consequence; the battery record names the top three consumers with figures; and every security symptom has a named cause and response.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
230

## Slide 231
LAB 48 · PROCESS MAP
How Lab 48 Runs
1
Order the escalation
Force close, cache, data, reinstall, then update
2
Know the difference
Clearing data resets the app and removes saved logins
3
Split battery drain
Background apps, weak signal, brightness or a dead cell
4
Reset the radios
Airplane mode, forget the network, re-pair the device
5
Read the security signs
Sideloaded APKs, root or jailbreak, spoofed apps
THE POINT
Diagnose and resolve mobile operating system and application faults including crashes, connectivity, battery and performance problems (Core 2 objectives 3.4 and 3.5).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
231

## Slide 232
LAB 48 · VERIFY
Mobile OS and Application Troubleshooting
✅ Expected result
Your sequence orders the five application steps from least to most destructive; the cache-versus-data distinction is stated with its consequence; the battery record names the top three consumers with figures; and every security symptom has a named cause and response.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
232

## Slide 233
TOPIC 08 · HANDS-ON
System Restore, Backup Verification and Recovery Testing
LAB 49
Configure System Restore and Windows backup, then verify recovery by performing an actual restore (Core 2 objectives 3.1 and 4.3).
An untested backup is not a backup. You configure protection and backup, then actually restore a file — because the restore is the only step that proves the whole chain works, and it is the step that gets skipped.
YOU'LL BUILD
A configured and verified backup with a completed restore test and a written recovery procedure.
TOOLCHAIN
Windows PC, System Protection, File History, Killercoda Ubuntu Playground, tar
DONE WHEN
A restore point is created and listed; the archive is created and the original data deleted; the restore returns both files; md5sum -c reports OK for every file; and your recovery procedure states the 3-2-1 rule with the threat each part defeats.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
233

## Slide 234
LAB 49 · PROCESS MAP
How Lab 49 Runs
1
Create a restore point
Confirm protection is on and the point is listed
2
Know its scope
System files and registry, but not your documents
3
Apply 3-2-1
Three copies, two media types, one kept off site
4
Work the arithmetic
Incremental needs five restores; differential needs two
5
Prove the restore
Delete, restore, then match the checksums
THE POINT
Configure System Restore and Windows backup, then verify recovery by performing an actual restore (Core 2 objectives 3.1 and 4.3).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
234

## Slide 235
LAB 49 · VERIFY
System Restore, Backup Verification and Recovery Testing
✅ Expected result
A restore point is created and listed; the archive is created and the original data deleted; the restore returns both files; md5sum -c reports OK for every file; and your recovery procedure states the 3-2-1 rule with the threat each part defeats.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
235

## Slide 236
TOPIC 08 RECAP · 23% of Core 2
Recap — Software Troubleshooting
• You can now: Diagnose common Windows symptoms and select the correct recovery tool, escalating from least to most destructive (Core 2 objectives 3.1 and 3.2).
• You can now: Filter and parse system logs with regular expressions to isolate the events that matter during troubleshooting (Core 2 objectives 3.1 and 4.8).
• You can now: Recognise malware and browser symptoms, apply the containment sequence and resolve browser-specific problems (Core 2 objectives 3.2 and 3.3).
• You can now: Diagnose and resolve mobile operating system and application faults including crashes, connectivity, battery and performance problems (Core 2 objectives 3.4 and 3.5).
• You can now: Configure System Restore and Windows backup, then verify recovery by performing an actual restore (Core 2 objectives 3.1 and 4.3).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
236

## Slide 237
TOPIC 09
Operational Procedures
Documentation and ticketing · asset management · change management · backup and recovery · safety and environment · professionalism · scripting and remote access
09
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
237

## Slide 238
CORE 2 · 21% OF CORE 2
Topic 09 at a Glance — Operational Procedures
1
Exam
CompTIA A+ Core 2
2
Domain weighting
21% of Core 2
3
Share of course time
5%
4
Hands-on labs
Lab 50, Lab 51, Lab 52, Lab 53, Lab 54
5
Sub-topics
Documentation and ticketing · asset management · change management · backup and recovery · safety and environment · professionalism · scripting and remote access
6
Why it matters
This domain is assessed in both the WSQ Written Assessment and the Practical Performance.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
238

## Slide 239
TOPIC 09 · 21% of Core 2
Key Concepts — Operational Procedures
1
A ticket is the unit of work and the audit trail. It must capture user and device information, a clear problem description, category, severity, escalation level, the steps attempted and the final resolution, written in plain professional language.
2
Asset management tracks what the organisation owns through inventory lists, asset tags and barcodes, the procurement life cycle, warranty and licensing status, and the user each asset is assigned to.
3
Documentation types each serve a purpose: acceptable use policies, network topology diagrams, standard operating procedures, new-user setup and end-user termination checklists, incident reports and knowledge-base articles.
4
Change management protects production. Every change needs a documented business process, a stated purpose and scope, a risk analysis, a scheduled date and time, an approval, a rollback plan and a sandbox test before it goes live.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
239

## Slide 240
TOPIC 09 · 21% of Core 2
Key Concepts — Operational Procedures (2)
1
The 3-2-1 backup rule requires three copies of the data on two different media with one copy off site, and it is the single most examinable backup fact in Core 2.
2
Backup types trade time against restore complexity. A full backup copies everything, an incremental copies what changed since the last backup of any type and clears the archive bit, and a differential copies what changed since the last full backup and leaves the archive bit set.
3
An untested backup is not a backup. Restore testing on a schedule is what proves the backup chain, the media and the documented restore procedure actually work.
4
Electrostatic discharge damages components at voltages far below what a person can feel, so use an anti-static strap and mat, hold cards by the edges, store parts in anti-static bags and equalise potential before touching a component.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
240

## Slide 241
TOPIC 09 · 21% of Core 2
Key Concepts — Operational Procedures (3)
1
Personal and electrical safety means disconnecting power before working inside a machine, never opening a power supply or CRT, using correct lifting technique, and knowing which fire extinguisher class is right for an electrical fire.
2
Environmental controls cover safe disposal of batteries, toner and devices under the relevant MSDS/SDS, temperature and humidity management, dust control, and protecting equipment with surge suppressors and an uninterruptible power supply.
3
Regulated data carries legal obligations: PII, PCI DSS for card data, GDPR for EU personal data, PHI under HIPAA for health data, and Singapore's PDPA — and the chain of custody must be preserved for anything that may become evidence.
4
Professional conduct is assessable: dress appropriately, use plain language rather than jargon, maintain a positive attitude, listen without interrupting, be culturally sensitive, avoid distractions, set realistic expectations and follow up afterwards.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
241

## Slide 242
TOPIC 09 · 21% of Core 2
Key Concepts — Operational Procedures (4)
1
Scripting automates repetitive support work — restarting machines, remapping drives, installing applications, running backups and gathering inventory — using .bat, .ps1, .vbs, .sh, .py or .js, with the risks of unintended system changes and browser or resource overload.
2
Remote access methods differ in security and use case: RDP for Windows desktops, VNC for cross-platform screen sharing, SSH for encrypted command line, VPN for network-level access, and third-party screen-sharing tools for supporting end users.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
242

## Slide 243
WHAT YOU'LL DO
Hands-On Labs — Operational Procedures
Labs 50–51
• Ticketing, Documentation and Knowledge Base Authoring
• Change Management and Asset Management
Labs 52–53
• Backup Strategy Design and the 3-2-1 Rule
• Safety Procedures, ESD Control and Environmental Compliance
Lab 54
• Professional Communication, Scripting and Remote Access
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
243

## Slide 244
TOPIC 09 · HANDS-ON
Ticketing, Documentation and Knowledge Base Authoring
LAB 50
Write support tickets and documentation to professional standard, and author a knowledge base article from a resolved incident (Core 2 objective 4.1).
A ticket is both the work record and the organisation's memory. You write a complete ticket from a real scenario, then convert it into the knowledge base article that stops the next technician re-solving the same problem from scratch.
YOU'LL BUILD
A completed support ticket meeting all required fields, and a knowledge base article derived from it.
TOOLCHAIN
Ticketing template, documentation standards reference, knowledge base template
DONE WHEN
Your ticket contains all nine required fields with a justified severity and escalation level; the diagnostic steps include at least one that ruled a cause out; and the knowledge base article has a searchable title, symptom, cause, numbered resolution and prevention note.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
244

## Slide 245
LAB 50 · PROCESS MAP
How Lab 50 Runs
1
Capture the ticket
User, device, symptom, category, severity and escalation
2
Separate the voices
The user's words, then your technical observation
3
Record what you ruled out
A negative result is evidence and belongs in the log
4
Write the resolution
Name the setting or component actually changed
5
Publish the article
Searchable title, symptom, cause, steps and prevention
THE POINT
Write support tickets and documentation to professional standard, and author a knowledge base article from a resolved incident (Core 2 objective 4.1).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
245

## Slide 246
LAB 50 · VERIFY
Ticketing, Documentation and Knowledge Base Authoring
✅ Expected result
Your ticket contains all nine required fields with a justified severity and escalation level; the diagnostic steps include at least one that ruled a cause out; and the knowledge base article has a searchable title, symptom, cause, numbered resolution and prevention note.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
246

## Slide 247
TOPIC 09 · HANDS-ON
Change Management and Asset Management
LAB 51
Prepare a change request with risk analysis, rollback plan and approval path, and maintain an asset register through the procurement life cycle (Core 2 objectives 4.2 and 4.1).
Change management is what stops a well-intentioned fix becoming an outage. You prepare a complete change request for a real change, then build the asset register that tells you what you actually own before you change any of it.
YOU'LL BUILD
A complete change request with risk analysis and rollback plan, plus an asset register covering the procurement life cycle.
TOOLCHAIN
Change request template, asset register template, organisational policy reference
DONE WHEN
Your change request contains all ten fields with a risk level that is justified rather than asserted; the rollback plan has specific steps; the approver is separate from the implementer; and the asset register covers all seven life cycle stages.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
247

## Slide 248
LAB 51 · PROCESS MAP
How Lab 51 Runs
1
Scope the change
Purpose, affected systems, and what is out of scope
2
Analyse the risk
Likelihood, impact, mitigation and a justified level
3
Test in a sandbox
Catch the incompatibility before it reaches 50 users
4
Plan the way back
A change with no rollback needs a stronger case
5
Separate the roles
The implementer must not approve their own change
THE POINT
Prepare a change request with risk analysis, rollback plan and approval path, and maintain an asset register through the procurement life cycle (Core 2 objectives 4.2 and 4.1).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
248

## Slide 249
LAB 51 · VERIFY
Change Management and Asset Management
✅ Expected result
Your change request contains all ten fields with a risk level that is justified rather than asserted; the rollback plan has specific steps; the approver is separate from the implementer; and the asset register covers all seven life cycle stages.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
249

## Slide 250
TOPIC 09 · HANDS-ON
Backup Strategy Design and the 3-2-1 Rule
LAB 52
Design a backup strategy specifying types, rotation, retention and off-site copy, and justify it against a stated recovery objective (Core 2 objective 4.3).
You design a backup strategy for a small business, choosing the backup types and rotation that meet a stated recovery point and recovery time objective — and then prove the design meets them by working the restore arithmetic rather than assuming it does.
YOU'LL BUILD
A complete backup strategy with schedule, rotation scheme, retention policy and a restore-time calculation proving it meets the objectives.
TOOLCHAIN
Backup strategy template, Killercoda Ubuntu Playground, backup type reference
DONE WHEN
Your strategy states both RPO and RTO and the schedule meets them; the restore arithmetic is worked for both incremental and differential; the choice is justified against the 4-hour RTO; and the design includes an offline or immutable copy and a stated restore test schedule.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
250

## Slide 251
LAB 52 · PROCESS MAP
How Lab 52 Runs
1
Set the objectives
How much data can be lost, and how long offline
2
Apply 3-2-1
Each element defeats a different class of failure
3
Compare the types
Full, incremental and differential on time and restore
4
Work the restores
Five operations against two for the same recovery
5
Protect from ransomware
One copy offline, air-gapped or immutable
THE POINT
Design a backup strategy specifying types, rotation, retention and off-site copy, and justify it against a stated recovery objective (Core 2 objective 4.3).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
251

## Slide 252
LAB 52 · VERIFY
Backup Strategy Design and the 3-2-1 Rule
✅ Expected result
Your strategy states both RPO and RTO and the schedule meets them; the restore arithmetic is worked for both incremental and differential; the choice is justified against the 4-hour RTO; and the design includes an offline or immutable copy and a stated restore test schedule.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
252

## Slide 253
TOPIC 09 · HANDS-ON
Safety Procedures, ESD Control and Environmental Compliance
LAB 53
Apply ESD, electrical and personal safety procedures, and comply with environmental requirements for disposal and equipment protection (Core 2 objectives 4.4 and 4.5).
Safety procedures are examinable and are the part of the job where a mistake injures someone or destroys equipment. You build the complete procedure covering ESD, electrical safety, personal safety and environmental compliance, and identify hazards in a real workspace.
YOU'LL BUILD
A workspace safety procedure covering ESD, electrical, personal and environmental requirements, with a completed hazard assessment.
TOOLCHAIN
Anti-static equipment, safety reference material, MSDS/SDS documentation, workspace
DONE WHEN
Your procedure covers ESD, electrical, personal and environmental safety; it explicitly forbids opening a PSU and a CRT and states why; Class C is named for electrical fires; and the hazard assessment lists real hazards with a control for each.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
253

## Slide 254
LAB 53 · PROCESS MAP
How Lab 53 Runs
1
Control static
Strap, mat, bags — damage happens below what you can feel
2
Handle by the edges
Never touch gold contacts or chip pins
3
Isolate the power
Unplug and discharge; never open a PSU or a CRT
4
Know the fire class
Class C for electrical; never water
5
Dispose correctly
Batteries, toner and e-waste under the relevant SDS
THE POINT
Apply ESD, electrical and personal safety procedures, and comply with environmental requirements for disposal and equipment protection (Core 2 objectives 4.4 and 4.5).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
254

## Slide 255
LAB 53 · VERIFY
Safety Procedures, ESD Control and Environmental Compliance
✅ Expected result
Your procedure covers ESD, electrical, personal and environmental safety; it explicitly forbids opening a PSU and a CRT and states why; Class C is named for electrical fires; and the hazard assessment lists real hazards with a control for each.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
255

## Slide 256
TOPIC 09 · HANDS-ON
Professional Communication, Scripting and Remote Access
LAB 54
Apply professional communication standards including handling difficult customers, and select appropriate scripting and remote access methods for support tasks (Core 2 objectives 4.7, 4.8 and 4.9).
This final lab covers the three areas that decide whether a technically correct technician is actually effective: how they communicate, how they automate repetitive work, and how they reach a machine they cannot physically touch.
YOU'LL BUILD
A professional communication guide with difficult-customer scenarios, an automation candidate list and a remote access selection matrix.
TOOLCHAIN
Killercoda Ubuntu Playground, communication scenario briefs, remote access reference
DONE WHEN
The inventory script runs and outputs all seven fields; both difficult-customer scenarios have written responses applying the stated rules; the matrix covers five remote access methods with port and security consideration; and the scripting risks are recorded.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
256

## Slide 257
LAB 54 · PROCESS MAP
How Lab 54 Runs
1
Set the standard
Plain language, no jargon, and a positive attitude
2
Listen and confirm
Restate the problem before you act on it
3
Handle the difficult call
Do not argue, dismiss or judge — clarify instead
4
Automate the repetition
Restarts, drive mapping, installs, backups and inventory
5
Choose the remote path
RDP, VNC, SSH, VPN or screen sharing, by need
THE POINT
Apply professional communication standards including handling difficult customers, and select appropriate scripting and remote access methods for support tasks (Core 2 objectives 4.7, 4.8 and 4.9).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
257

## Slide 258
LAB 54 · VERIFY
Professional Communication, Scripting and Remote Access
✅ Expected result
The inventory script runs and outputs all seven fields; both difficult-customer scenarios have written responses applying the stated rules; the matrix covers five remote access methods with port and security consideration; and the scripting risks are recorded.
IF IT DOESN'T WORK
A step won't run
Re-read the step in the Learner Guide — it carries the full detail the slide summarises.
A browser tool won't load
Check the URL against the Lab Tool Links slide; all four tools run client-side and need no login.
Killercoda has reset
The playground times out when idle. Reopen it and re-run the setup commands from the start of the lab.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
258

## Slide 259
TOPIC 09 RECAP · 21% of Core 2
Recap — Operational Procedures
• You can now: Write support tickets and documentation to professional standard, and author a knowledge base article from a resolved incident (Core 2 objective 4.1).
• You can now: Prepare a change request with risk analysis, rollback plan and approval path, and maintain an asset register through the procurement life cycle (Core 2 objectives 4.2 and 4.1).
• You can now: Design a backup strategy specifying types, rotation, retention and off-site copy, and justify it against a stated recovery objective (Core 2 objective 4.3).
• You can now: Apply ESD, electrical and personal safety procedures, and comply with environmental requirements for disposal and equipment protection (Core 2 objectives 4.4 and 4.5).
• You can now: Apply professional communication standards including handling difficult customers, and select appropriate scripting and remote access methods for support tasks (Core 2 objectives 4.7, 4.8 and 4.9).
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
259

## Slide 260
WRAP-UP
Course Summary & Next Steps
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
260

## Slide 261
LEARNING OUTCOMES
What You Achieved
1
LO1 · Diagnosed and resolved
Applied the six-step methodology to hardware, network, OS and application faults, resolving root causes rather than symptoms.
2
LO2 · Troubleshot and configured
Configured SOHO networks, RAID, BIOS/UEFI, Windows security, Linux permissions and mobile device management.
3
LO3 · Planned upgrades
Produced memory, storage, power and backup upgrade plans justified against real requirements and constraints.
4
LO4 · Tested and documented
Verified every lab against a stated success criterion and produced tickets, runbooks and knowledge base articles.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
261

## Slide 262
NEXT STEPS
Your Certification Path
1
Step 1 · Core 1 (220-1101)
Mobile devices, networking, hardware, virtualization and cloud, hardware and network troubleshooting.
2
Step 2 · Core 2 (220-1102)
Operating systems, security, software troubleshooting and operational procedures.
3
Both required
You must pass both exams to earn the CompTIA A+ certification. They are sat separately.
4
Practice first
Sit the practice exam at https://exams.tertiaryinfotech.com and revise the domains where you scored lowest.
5
Rebuild the labs
Redo each lab from a blank sheet until the diagnostic sequence is automatic rather than looked up.
6
Keep the tools
The four browser tools and the Killercoda playground stay free — use them to keep the skills current.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
262

## Slide 263
FREE · NO INSTALL · KEEP USING THEM
Keep Practising — Your Lab Toolkit
1
IP Calculator
https://alfredang.github.io/ipcalculator/
2
PCAP Analyzer
https://alfredang.github.io/pcapanalyzer/
3
Cybersecurity Simulator
https://alfredang.github.io/cybersecuritysimulator/
4
RegexLab
https://alfredang.github.io/regexgenerator/
5
Killercoda Ubuntu Playground
https://killercoda.com/playgrounds/scenario/ubuntu
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
263

## Slide 264
CONTINUE WITH TERTIARY INFOTECH
Recommended Courses
1
WSQ - CompTIA Certified Network+ Training
2
WSQ - CompTIA Certified Security+ Training
3
WSQ - CompTIA Certified Server+ Training
4
WSQ - CompTIA Certified Linux+ Training
5
WSQ - CompTIA Certified Cloud+ Training
6
WSQ - CompTIA PenTest+ Training
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
264

## Slide 265
WE'RE HERE TO HELP
Support
• If you have any enquiries during or after the class, you can contact us below.
• Email: enquiry@tertiaryinfotech.com
• Tel: +65 6100 0613
• Website: www.tertiarycourses.com.sg
• LMS / TMS: https://lms-tms.tertiaryinfotech.com
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
265

## Slide 266
WRAP-UP
Assessment
1
Written Assessment (SAQ)
1 hour · open book · short-answer knowledge questions across the nine domains.
2
Practical Performance (PP)
1 hour · open book · hands-on support, configuration and troubleshooting tasks.
3
Digital attendance
Remember to take the Assessment digital attendance (TRAQOM) before you start.
4
Submit on the LMS
Upload your completed answers at https://lms-tms.tertiaryinfotech.com/
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
266

## Slide 267
ON ASSESSMENT DAY
Assessment Flow
1
TRAQOM survey
Scan the QR code on the LMS
2
Digital attendance
Scan the SSG assessment QR
3
Sit WA then PP
Open book · 1 hour each
4
Submit on the LMS
Upload your completed answers
5
Sign the record
Sign the Assessment Summary Record
REMEMBER
All five steps are mandatory for WSQ funding — missing the digital attendance or the TRAQOM survey can invalidate your claim.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
267

## Slide 268
TRAQOM · SSG DIGITAL ATTENDANCE
Digital Attendance (Mandatory)
1
Three times a day
Take the AM, PM and Assessment digital attendance — mandatory for every WSQ-funded course.
2
Trainer shows the QR
The trainer or administrator displays the digital attendance QR code from the SSG portal.
3
Scan and submit
Scan the QR code with your mobile phone camera and submit your attendance.
4
75% minimum
A minimum of 75% attendance is required to be eligible for assessment and funding.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
268

## Slide 269
GOOD LUCK IN YOUR EXAMS
Thank You!
You can now diagnose, configure, secure and document the hardware, networks, operating systems and mobile devices an IT support role depends on.
CompTIA-Certified-A-Training-Core-1-and-Core-2 · TGS-2024048317
© 2026 Tertiary Infotech Academy Pte Ltd
269